## Slide 1
ITSC 204:
Computer Architecture
Module 1: Architecture of General Purpose Processor
Notes: 1

## Slide 2
Computer Architecture
There are two major architecture used to explain or interpret the design(s) used in the manufacturing of computers. They describe how the hardware components can be placed to perform the necessary computation in a stored-program system. They are as follows:
  von Neumann Architecture
  Harvard Architecture
It is not guaranteed that manufacturers will use exactly the designs as presented, but the overall behavior will following one of the above. In some cases they may combine them to get better performance or lower costs.
Both have been around for many years and have been the base of countless computer systems.

## Slide 3
von Neumann Architecture
Von Neumann proposed a computer architecture with six elements:
    Central Arithmetic unit (CA)
    Central Control unit (CC)
    Memory (M)
    Input (I)
    Output (O)
    Slow memory (R) – think external storage, such as magnetic tapes and punched cards

## Slide 4
von Neumann Architecture
Notes: Abstraction

## Slide 5
von Neumann Architecture
The diagram below shows the general layout of the von Neumann architecture.
This Photo by Kapooht is licensed under CC BY-SA
More information can be found here: https://en.wikipedia.org/wiki/Von_Neumann_architecture
Notes: Abstraction

## Slide 6
von Neumann Architecture
The von Neumann architecture is distinguishable through the following characteristics
Advantage:
  Simplicity easier to manufacture
  As a result more economical
Disadvantage
  Uses 1 bus to retrieve data and instruction, creates a challenge for pipelining
  Uses a single memory space for both data and instructions, often making it difficult to determine which you are looking at.
Using a single space for both data and instructions creates a challenge for debugging tools. Why???

## Slide 7
Harvard Architecture
The Harvard architecture is identifiable by a few characteristics:
Implemented for DSP (Digital Signal Processing)
Advantage
  They have separate data and instruction memory
  It can fetch an instruction and data words simultaneously
  Both instruction and data can be read every clock cycle
Disadvantage
  Requires more logic to implement
  More bus lines to accomplish
This Photo by Nessa Los is licensed under CC BY-SA
https://en.wikipedia.org/wiki/Harvard_architecture

## Slide 8
Processor Manufacturers/Designers
The most common x86 processor manufactures are:
Intel Compatible Processors
  Intel: https://www.intel.ca/
  AMD: https://www.amd.com/
ARM Processors
  ARM: https://www.arm.com/
  ARM based : Raspberry pi https://www.broadcom.com/

## Slide 9
Multicore/Multithread Processors
Quad Core Intel Processor
https://intel.ca

## Slide 10: Why Number Systems ?
Throughout human existence there have been many attempts made to create a way to quantify the world around us. That has led to the creation of many number systems. Numbers are especially relevant in the computer world where the machine only understands numbers. They are an important primitive that is foundational to identifying what is data and instructions used within the computer logic.
The most common numerical systems are:
  Decimal system
    0,1,2,3,4,5,6,7,8,9
    Power of 10
  Computers implement binary , hexadecimal and Octal systems
    1. Binary system - Base 2
      0,1
      Powers of 2
    2. Hexadecimal system
      0,1,2,3,4,5,6,7,8,9,A,B,C,D,E,F
      Powers of 16
    3. Octal is not often seen or used beyond theory.

## Slide 11
Counting …
Below is an example of counting within various number systems.
Decimal (base 10) | Binary (base 2) | Hexadecimal (base 16) | Octal (base 8) | Gray Code
0 | 0000 0000 | 0x00 | 000 | 00000
1 | 0000 0001 | 0x01 | 001 | 00001
2 | 0000 0010 | 0x02 | 002 | 00011
3 | 0000 0011 | 0x03 | 003 | 00010
4 | 0000 0100 | 0x04 | 004 | 00110
5 | 0000 0101 | 0x05 | 005 | 00111
6 | 0000 0110 | 0x06 | 006 | 00101
10 | 0000 1010 | 0x0A | 012 | 01111
11 | 0000 1011 | 0x0B | 013 | 01110
12 | 0000 1100 | 0x0C | 014 | 01010
13 | 0000 1101 | 0x0D | 015 | 01011
14 | 0000 1110 | 0x0E | 016 | 01001
15 | 0000 1111 | 0x0F | 017 | 01000
16 | 0001 0000 | 0x10 | 020 | 11000

## Slide 12
2’s Twos Complement
The 2’s complement is a technique used to simplify ADD and SUB arithmetic operations. The problem being solved is how to deal with signed numbers (positive 0 and negative 1).
By convention the most significant bit represents the sign. Adding and subtracting binary negative numbers can generate an error by the carry or overflow bit
So how does one find the negative value of a binary number - 2’s complement.
Find 1’s first complement which is the negation of the bit.
1’s complement flips or inverts the individual bits in a number; such that:
0 becomes 1 and 1 becomes 0
See example calculation to the right is for 1110 0110
Finally, add 1 to the 1’s first complement
The binary number 0001 1010 is decimal 26.
The MSB from the original number was 1 therefore the
final number is -26.
Notes: The negative sign can’t be stored in memory with the number, so how does the system quantify that data?
The binary number represents a number you found in memory and want to know what negative number is represented

## Slide 13
Nibble - Signed numbers
Positive Negative
1 0001 -1 1111
2 0010 -2 1110
3 0011 -3 1101
4 0100 -4 1100
5 0101 -5 1011
6 0100 -6 1010
7 0111 -7 1001
0 0000 -8 1000
Sign Magnitude
Binary Negative Numbers

## Slide 14
Binary System Grouping
To make sense of the number we deal with on an ongoing basis we need to have units that we will refer to. Common data sizes often encountered are as follows:

## Slide 15
Why Binary?
Could the early researchers (Physicist and Engineers) have used the common number system known to everyone?
Some arguments exist that yes it would have been possible, but the cost to do so may have been prohibitive. As well it may have cost us in terms of our ability to miniaturize our electronics. Binary numbers, from the perspective of the circuits used to create the computers, allow for a fraction of the power previously used. The reason for that is the invention of the transistor.
Watch https://www.youtube.com/watch?v=thrx3SBEpL8

## Slide 16
What is a transistor?
Transistor - a semiconductor device used to amplify or switch electronic signals and power. The transistor turns on and off, based on a voltage applied to one of its inputs.
For more details read: https://en.wikipedia.org/wiki/Transistor and
https://www.digikey.ca/en/articles/techzone/2017/dec/transistor-basics
watch: https://www.youtube.com/watch?v=qUeK7pHe0rI
This Photo is licensed under CC BY-SA
This Photo is licensed under CC BY-SA
This Photo is licensed under CC BY-SA

## Slide 17
MOSFET Transistors
Metal Oxid Semiconductor Field-Effect Transistor (MOSFET) is the compact silicon transistor that has been miniaturised and mass-produced for many applications. It is implemented It has four pins Source(S), Gate(G) and Drain(D) and Body(B)
It can be made with either p-type or n-type then it can be use to make switching circuits with very low power.
It is the most widely manufactured device in history. How many of this transistor had been manufactured?

## Slide 18
Transistors Transform …
What would happen if a single transistor was combined with other transistors?
Expanding on the idea of a single transistor seemed to be the next logical step. Placing them in different configurations allowed for the creation of complex circuits which could perform far more operations than simply switching on and off.
This Photo by EBatlleP is licensed
under CC BY-SA
This Photo by EBatlleP is licensed
under CC BY-SA
This Photo of a NOT Gate by Pradana Aumars is licensed under CC BY-SA

## Slide 19
Abstraction of Logic
Once a basic understanding of the core circuit that performs the logic is clear; drawing circuits for every single situation becomes overwhelming. This all can be abstracted using building blocks to show the overall logic of what is happening.
This Photo by Lambtron is licensed under CC BY-SA
Arithmetic Logic Unit (ALU)
This Photo by Pdesousa359 is licensed under CC BY-SA
Circuit Diagram of Full Adder
This Photo by Lambtron is licensed under CC BY-SA

## Slide 20
In digital systems the signals are formed with two voltage values, HI and LOW, or level 1 and level 0 and it is called binary digital signal. Therefore, the information contained in the digital signal is represented by the numbers 1 and 0.
Each digit of a binary number, 0 or 1, is called a bit, an abbreviation for binary digit
bit 1 or 0
Binary in Logic

## Slide 21
Binary in Logic
Most computers operate with two voltage levels
  Logic 0: (typically represented by voltage of 0)
  Logic 1: (which can have varying values)
    5V (Transistor to Transistor Level Logic, used in first microprocessors)
    3.3V (In older cores, most I/O pads on System on a Chip (SoC))
    2.5V (newer cores)
    1.8V (newer cores, DRAM bus, some SoC pads)
    0.85V (Intel Pentium M core in Battery Optimized Mode)
  binary one = +5 volts
  binary zero = 0 volts
Be careful in how you connect devices which can vary in voltage requirements from your test circuits. Remember everyone will LET THE SMOKE OUT!!!!
Try not to do so with expensive electronics!!!

## Slide 22
Gordon Moore, Intel founder, proposed silicon technology and his Moore’s Law states that the number of transistors that can be placed on a given cheap area doubles approximately every two years. The original Intel processor had 2300 transistors and Pentium 4 has around 42 million.
The capability of reducing the size of electronic circuits serves to reduce chip cost.
To find more information about Moore’s Law access the following web site: https://www.intel.com/content/www/us/en/history/museum-gordon-moore-law.html
Moore’s Law

## Slide 23
Processor Building Blocks
There are many components that make up a processor. Nevertheless, we will use a simplified design to gain a high-level view of the structure of the Processor.
The basic building blocks of a processor are as follows:
  Arithmetic Logic Unit (ALU)
  Instruction Decoder
  Control Unit
  Registers (Register File)
  Bus (Data and Address)
There are many more components that allow the processor to perform its job. The aforementioned will be discussed further. Learn more from the following link: https://en.wikipedia.org/wiki/Central_processing_unit

## Slide 24
Generic CPU - Internals
This Photo is by stackexchange licensing to be determined

## Slide 25
The ALU component in the CPU is responsible for performing integer arithmetic and logical operations as requested by instructions from the program in execution. Adder circuits can handle both addition and subtraction and integer multiplication is presented as repeated shift-and-add operations.
Floating point arithmetic can be performed by software routines that rely on the integer machine instructions and the ALU. Now floating-point arithmetic can be performed by hardware known as FPU (Floating-point Unit). Pentium has all arithmetic calculations integrated into the main CPU. The common for floating-point numbers is now IEEE 754 for 32, 64 and 128 bit numbers
Arithmetic Logic Unit

## Slide 26
Arithmetic Logic Unit
The ALU says it all, it is the basic computation unit within the processor. It generally operates on 2 operands and executes the following instructions:
  ADD, SUB ( Arithmetic Operations)
  OR, AND, XOR, NOT (Logical Operations)
  Sets the Status Flags based on the those operations
    Zero
    Carry
    Overflow
    more
  It uses the Status Flags to determine:
    Arithmetic and Logic validity in output
    Fault in execution (Trap)

## Slide 27
AND Logic Gate
This Photo by EBatlleP is licensed
under CC BY-SA
This Photo by EBatlleP is licensed
under CC BY-SA
Truth Table

## Slide 28
Bitwise AND Logic operation
Let’s calculate the Logical AND
21 &179
Decimal 21 is 0001 0101 as a binary number
Decimal 179 is 1011 0011 as a binary number

## Slide 29
OR Logic Gate
This Photo by EBatlleP is licensed
under CC BY-SA
This Photo by EBatlleP is licensed
under CC BY-SA
Truth Table
This Photo by EBatlleP is licensed
under CC BY-SA

## Slide 30
Bitwise OR Logic operation
Let’s calculate the Logical OR
21 | 179
Decimal 21 is 0001 0101 as a binary number
Decimal 179 is 1011 0011 as a binary number

## Slide 31
XOR Logic Gate
This Photo by EBatlleP is licensed
under CC BY-SA
Truth Table
This Photo by EBatlleP is licensed
under CC BY-SA

## Slide 32
Bitwise XOR Logic operation
Let’s calculate the Logical OR
21  179 alternatively 21 ^ 179
Decimal 21 is 0001 0101 as a binary number
Decimal 179 is 1011 0011 as a binary number
Let’s calculate the Logical OR
255  255 alternatively 255 ^ 255
Decimal 255 is 1111 1111 as a binary number
Decimal 255 is 1111 1111 as a binary number
XOR value can be used to clear registers or memory location
XOR can be used to test for equality

## Slide 33
NOT Logic Gate
This Photo by EBatlleP is licensed
under CC BY-SA
Truth Table
This Photo by EBatlleP is licensed
under CC BY-SA
Let’s calculate the Logical NOT of 21
Logical NOT is the same as 1’s Complement)

## Slide 34
ADDER Logic circuit
This Photo by Inductiveload is licensed under CC BY-SA
This Photo by Inductiveload is licensed under CC BY-SA
This Photo by Inductiveload is licensed under CC BY-SA
1 BIT ADDER
This Photo by GD is licensed under CC BY-SA 4 BIT ADDER

## Slide 35
For signed numbers if carry bits (last two most significant bits) are the same 11 or 00 the result is correct or valid but if the last two carry bits are different 01 or 10 then the system creates sign overflow. In this case 1000 0110 for signed numbers the result represents a negative value of (-122). For unsigned numbers the most significant bit is part of the number means the result will be 134 which is correct.
ADD Arithmetic operation

## Slide 36
How computers add number
ADD Arithmetic operation
https://www.youtube.com/watch?v=VBDoT8o4q00

## Slide 37
Subtractor Logic circuit
This Photo by Inductiveload is licensed under CC BY-SA
Circuit Diagram for half subtractor
This Photo by Inductiveload is licensed under CC BY-SA
Truth Table

## Slide 38
SUB Arithmetic operation

## Slide 39
Instruction Decoder
The CPU fetches instructions from memory. An instruction is a stream of bits to be decoded, to tell the CPU what to do. The structure of the instruction follows a predefined format, which is a part of the Instruction Set Architecture (ISA).
The instruction decoder is the unit that performs that job of understanding what instruction is being requested and if operands are needed, decides where to get them from (register, memory or immediate values). Once decoded those instructions are fed into other parts of the processor to continue performing its task.

## Slide 40
Control Unit
The Control unit is the director of operations for the processor. It ensures the orderly flow of information, telling other components what to do. This is done while also ensuring the synchronizing of all functions. It generates signals to control the communication between CPU and memory. It enable paths when decoding and executing operations. For example if a register value need to be added to second register in the CPU then the control unit will enable the path and the mode that allows to read and transmit the data from register to
ALU. After ALU add the values the control unit needs to enable the path that connect the ALU with the destination registry.
See: https://en.wikipedia.org/wiki/Control_unit

## Slide 41
Registers
Registers, also referred to as Register File are high speed memory areas with the CPU. They provide the storage locations for the data crunching components of the CPU. They hold temporary data required during operation.
They are usually the width of the architecture. In other words if, the system is a 32 bit system they are 32 bits wide. If the system is 64 bit architecture, the register sizes are 64 bits wide. There is the possibility of having 16 bit registers usually for segments.
In older architecture there numbers were limited. This is likely due to a few factors:
  Cost to add more, making the processor expensive
  Increase in size of the processor footprint

## Slide 42
Registers
As manufacturing processes have improved so has the number of registers possible to place on a die. For example in the newer 64 bit processor x86_64, it is likely to find some of the following registers:
RAX, RBX, RCX, RDX, RDI, RSI, RBP, RSP, R8-R15
  Compared to x86 EAX, EBX, ECX, EDX, EDI, ESI, EBP, ESP
Floating point registers also exist
Special purpose registers (RIP vs EIP, and RFlags vs EFlags)
Read more here: https://en.wikipedia.org/wiki/X86
What is a "die": https://en.wikipedia.org/wiki/Die_(integrated_circuit)

## Slide 43
Bus
The bus is the information highway within the processor. It provides a channel to transport data and instructions in and out of the processor.
The bus is a wide as the architecture, so for a 32 bit architecture the bus is 32 bits wide, therefore 32 parallel lines.
The number of lines gives the processor the ability to access up 232 x 1 byte per memory locations. This works out to be 4GB of information (instructions or data for those instructions).
Manufacturers won't necessary provide that many bus lines. Due to cost, practicality of doing so or the overall footprint not being available.
If there were 64 lines of data bus how much data could be accessed?
Read more here: https://en.wikipedia.org/wiki/Intel_80486

## Slide 44
How does the CPU work ?
https://www.youtube.com/watch?v=cNN_tTXABUA
How does the CPU work ?

## Slide 45
Instruction Set Architecture (ISA)
A subcategory of computer architecture is Instruction Set Architecture (ISA)
The computer hardware as shown so far is quite impressive but it needs instructions to accomplish any task that the end user requires.
The Instruction Set Architecture (ISA) is set of instructions available to the end user to tell the processor what to accomplish. It will follow a certain format ensuring that when it is applied to the hardware there is no misunderstanding.
  https://en.wikipedia.org/wiki/Instruction_set_architecture

## Slide 46
It is also an abstraction of the hardware features and is hardware implementation agnostic. Therefore if the ISA follows the rules of the CPU, it will be understood and processed.
There are two major ISA classifications we will refer to:
  Complex Instruction Set Computer (CISC)
  Reduced instruction Set Computer (RISC)
Instruction Set Architecture (ISA)

## Slide 47
Complex Instruction Set Computer
The Complex Instruction Set Computer CISC is an ISA that focuses on few instructions. It does so by having more complex instructions that may require more clock cycles but produce smaller programs.
Emphasis on fewer instructions translates to:
Less Memory required to store the program
More complex hardware
  Need specialized hardware to decode instruction.
Less registers due to direct access to memory
No specialized instructions for loading and storing
Less efficient pipeline

## Slide 48
Reduced Instruction Set Computer
The Reduced Instruction Set Computer RISC is an ISA that focuses on fewer clock cycles. It does so by having fewer and simpler instructions that can be executed relatively quickly.
Emphasis on fewer instructions translates to:
Writing efficient software
  More steps required to perform complex calculations (therefore write better code compiler or assembly).
  Large code size
More registers required to speed up execution, more memory operations
Special instructions for accessing memory
More efficient pipeline

## Slide 49
CISC vs RISC Comparison
ISA architectures differences:
RISC | CISC
Emphasis on Software | Emphasis on Hardware
Single clock cycles | Multiple clock cycles
Simple instructions | Complex instructions
Higher Register count | Lower Register count
Fix Instruction Set length ( 4 bytes=32 bits ) | Variable Instruction Set length (x86 1-15 Bytes)
Specialized Load and Store | No specialized Loads and Store
Larger code size | Smaller code size
Register File larger real estate | Large Microcode real estate

## Slide 50
CISC vs RISC Comparison - Assembly

## Slide 51
a=a+b result will be in variable a. Assuming a=5 and b=8
rax= 0x1240abdd ; rax contains the address of variable a
rdx = 0xab1234aa ; rdx registry contains the address of variable b
mov (%rdx), %edx ; copies the value in the location pointed by the address of rdx into registry edx. Means copy 8 to register edx. edx=*rdx
rdx rax edx
0xab1234aa 0x1240abdd 8
Label: a
0xab1240abdd
Label: b In Memory
0xab1234aa
add %edx, (%rax) ; Add to register edx the value located in memory address pointed by register rax
edx= 8 + 5 = 13
5
8
CISC – Assembly

## Slide 52
CISC vs RISC Comparison - Summary
From the previous slide we can conclude:
RISC processor requires more instructions
  6 instructions to complete the addition
  24 bytes – (the uniform width opcodes bytes add them)
CISC processor
  2 instructions to complete addition
  4 bytes in size – (the uniform width opcodes bytes add them)
Calculate the run time of the program based on the formula below.
Hint: Time / cycle is one period of the CPU. What is the period of a 1GHz processor.
RISC vs CISC Processors
https://cs.stanford.edu/people/eroberts/courses/soco/projects/risc/risccisc/

## Slide 53
CISC vs RISC Comparison - Code
gcc has 4 primary optimization levels: 0 - 3.
Level 0 being the least optimized
Level 3 being the most.
Other level exists s, g
Read more here: https://gcc.gnu.org/onlinedocs/gnat_ugn/Optimization-Levels.html

## Slide 54
The fetch-decode-execute cycle is the process by which the CPU retrieves the next instructions of the program from memory, decodes it and executes it.
Fetch-decode-execute cycle has many microcycles generated by the system clock. For a 200 Mhz clock the microcycle period is 5 ns (nanoseconds).
Period = 1/frequency = 1/200 microseconds (µs)= 1000/200ns= 5ns
Fetch-Decode-Execute cycle or
Instruction Cycle

## Slide 55
https://commons.wikimedia.org/wiki/File
Fetch-Decode-Execute_Cycle.png
Fetch-Decode-Execute cycle

## Slide 56
Fetch Phase
Program counter (PC) or Instruction Pointer (IP) contains the address of the next instruction to be executed. In the first clock cycle (T-0) The content of PC (which is an address) will be copied into the Memory Address Register (MAR) and transfer to memory module via Address Bus
In the next clock cycle T-1 the instruction located in memory (memory content –data) at the address pointed by PC is fetched and transferred via Data Bus from memory to CPU and stored in the Memory Data(Buffer) Registry (MDR or MBR). The content of MBR is now copied into Instruction Registry(IR) for the decoder to decipher it in the second phase
Fetch-Decode-Execute cycle

## Slide 57
3. AT the same T-1 clock pulse when data from memory is stored in IR, the PC or IP value is incremented by 1 (PC+1) to point to the next instruction. The PC should contain the address of the next instruction to be fetched
Instruction Register (IR) contains instruction to be decoded and executed.
Fetch Phase
OPERATION CODE OPCODE | Address Mode (Direct 0 or Indirect 1 ) | Operands

## Slide 58
Decode Phase
At clock cycle T-2 the Control Unit decodes the instruction in IR as per opcode. The control unit first has to decode the type of instruction:
    Memory reference
    Register reference or
    Input / Output Instruction
At clock cycle T-3 If the instruction is type memory reference the decoder will decode the mode address. If the mode address bit is 0 is a direct reference if the bit is 1 the memory reference is indirect.
Decoding in modern processors is done in parallel and it can be done out-of-order
Decode Phase

## Slide 59
Execute Phase
At clock pulse T-4 based on decoder information, the ALU will execute decoded operation with respective Flags
For memory reference if it is a direct reference it will execute the operation on the data located at memory address decoded in the instruction. If the reference is indirect then the effective address is located first then the operation is executed on the data located at that address
After execution is completed for the current instruction, the control is passed to Fetch phase to repeat the process for the next instruction pointed by PC
Execute Phase

## Slide 60
Understanding Transaction
Look at how the processor moves data around using the Generic CPU diagram. Below is a simplified view of the internals of the CPU and simplified connection to RAM.

## Slide 61
Assembly Instructions

## Slide 62
Assembly Instructions

## Slide 63
Assembly Instructions

## Slide 64
Assembly Instructions

## Slide 65
Fetch-Decode-Execution Cycle e.g.
Memory data (buffer) register
IR
PC or IP Memory Address register
0x b8 05
0x00401000
0x00401000
0x b8 05
DECODER
Control Unit (CU)
0xb8 05
0x48 ff c0
0xb8 3c
0xbf
0x0f 05
0x00401000
0x00401005
0x00401008
0x0040100d
0x00401012
Control Bus
Address Bus
MBR
MAR
Data Bus
RAX 0x6
Memory
CPU
ADDRESS
DATA

## Slide 66
https://en.wikipedia.org/wiki/Instruction_pipelining
Instruction Cycle in Pipeline Systems

## Slide 67
References
Here are a few resources to get a deeper understanding of the concepts:
  https://www.youtube.com/watch?v=LWjTIrxVS3Y
  https://www.youtube.com/watch?v=KIjoJSJ6OS8
  https://www.youtube.com/watch?v=1KTW32xSs_k
  https://www.youtube.com/watch?v=qm67wbB5GmI