## Slide 1
ITSC 204:
Computer Architecture
Module 2: Examine the x86 Hardware Architecture
Notes: 1

## Slide 2
Intel IA-32 and 64 Hardware Architecture
Processor | year | registers | Clock rate | Data/Address Width | Transistors | New features
4004 | 1971 | 8 bits: 16 registers | 740 kHz | Data 4 bits address 12 bits multiplexed Same bus for both | 2,250 | First random logic circuit integrated (IC) in one chip using the metal–oxide–semiconductor (MOS) 4 bit BCD
8086/8088 (x86) | 1979 | 16 bits: 16 General-Purpose (GP) registers and Segment registers | 6-10 MHz | Data 16 bits and address 20 bits | 29,000 | 16-bit segment register contains a pointer to a memory segment of up to 64 KBytes. ISA x86- 16
286 | 1982 | 16 bits: 8 GP and segment registers DS,CS, SS | 5 MHz to 25 MHz | Data 16 bits and address 24 bits | 134,000 | Introduced Protected mode that uses the segment register content as selectors or pointers into descriptor tables and new instructions added ISA x86- 16 with Memory Management Unit (MMU) able to address up to 16MB of RAM

## Slide 3
Intel 4004 Architecture

## Slide 4
Intel IA-32 and 64 Hardware Architecture
Processor | year | registers | clock | Data/Address Width | Transistors | New features
386 x86 IA-32 | 1985 | 32 bits: General registers EAX EBX ECX EDX Index and pointers ESI EDI EBP EIP ESP Segment registers CS DS ES FS GS SS Indicator EFLAGS | 30 MHz, 25 MHz, 20 MHz, 16 MHz | Data: 32 bits Address: 32 bits | 275,000 | The lower half of each 32-bit Intel386 register retains the properties of the 16-bit registers of earlier generations, permitting backward compatibility. Fro protected mode Paging and segment of 32 bit offset added Coprocessor x87 for Floating-point (FPU) calculations. The x87 provides single-precision, double-precision and 80-bit binary floating-point arithmetic -IEEE 754-1985
Pentium (greek means 5) I586 | 1993 | 32 bits registers | 60–66 MHz | Data 64 bits Address 32 bits | 3.1 Million | Two pipelines, known as u and v, together can execute two instructions per clock Added Cache L1

## Slide 5
Intel Pentium Architecture

## Slide 6
Intel IA-32 and 64 Hardware Architecture
Processor | year | registers | Clock rate | Data/Address Width | Transistors | New features
P6 Family | 1995 1999 | 32 bits registers | 66MHz-133Mhz | Data 64 bits Address 32 bits | 5.5 Million | Add 256KB cache L2 and increase its sizes. Parallel processing techniques that allows decode, dispatch, and complete execution of (retire) three instructions per clock cycle. introduced MMX technology that uses the single-instruction, multiple-data (SIMD) execution model to perform parallel computations on packed integer data contained in 64-bit registers.
Pentium 4 | 2000 |  | 1.3 GHz to 3.8 GHz | Data 64 bits Address 32 bits | 42 Million for – 188 M for 65 nm | Intel 64 architecture was introduced in the Intel Pentium 4 Processor Extreme Edition supporting Hyper-Threading. Virtualization Technology (Intel® VT) was introduced

## Slide 7
Intel IA-32 and 64 Hardware Architecture
Processor | year | registers | clock | Data/Address Width | Transistors | New features
Intel Core Multi-core technology Core,Core 2 Core i3, i5,i7 and i9 | 2006 Now | 64 bits registers | 1.6 GHz 10th Gen (core i9) chips 5.0GHz clock | Data 64 bits Address 32/64 bits | ~ 7 billion latest architecture | Core i3, i5 and i7 supports 2, 4 some releases support 6-8 cores such as coffee lake. Core i9 support 6-8 cores. It supports virtualization Intel's VT-x with EPT since 2008. Hyper-Threaded Intel 64 architecture L1, L2 and L3 Smart Cache to improve communication between cores and integrated memory controller.

## Slide 8
Intel Core i7

## Slide 9
Processors use either Big or little Endian format to store numbers
Intel 64 and IA-32 processors are “little endian” machines; this means the bytes of a word are numbered starting from the least significant byte.
ARM processor supports both formats
e.g 0x01020304
0x04030201 Little Endian 0x01020304 Big Endian
In Memory
04
02
01
03
01
04
03
02
Big Endian vs Little Endian

## Slide 10
Intel Data Types

## Slide 11
Registers
Computers perform many calculations per seconds, those calculations are performed by the ALU of the CPU. There are times when the end results of those calculations are required for other operations. For example, to access the address we may need to add an offset to the address. Or we may need to perform summation of multiple numbers.
Where does the ALU store those intermediate results, while we decide the next actions to perform. The likely response is in memory; RAM, possibly to the hard drive. Both are locations outside of the processor and both slower mediums for storing data. That means the potential for some bottleneck or latency in completing a fairly straightforward calculation.
To the rescue, comes the register!!!

## Slide 12
What is a register
A register is a high speed memory region on the CPU. The register is an abstraction but keep in mind that like other CPU components, this is also comprised of circuits that can be switched on and off and hold data via a process called latching. Some characteristics of registers are as follows:
  As wide as the architecture bus (16, 32, 64 bits)
  Used as temporary stores for the CPU's ALU
    Storing computation results and addresses for example
  Information can be written to and read from them
  Data can be copied between registers
Interested Watch more here: https://www.youtube.com/watch?v=fpnE6UAfbtU
Essentials of Computer Organization and Architecture, 5th Ed. – Section 4.2.1 - The registers
Interesting reading: https://en.wikipedia.org/wiki/Hardware_register

## Slide 13
Register and Architecture
The number and types of registers will vary from model to model and architecture to architecture. Nevertheless, most modern text books dealing with Intel x86 processor (32 bits) will outline the following:
General purpose registers
  These are registers that can be used for any purpose required to complete a task.
  They are (EAX, EBX, ECX, EDX, ESI, EDI, ESP, EBP)
  These registers can hold operands for logical and arithmetic operations, operands for address calculations and memory pointers
2. Special Purpose registers
  EIP and EFLAGS registers have a special purpose and cannot be used directly by any user level instructions.
3. Segment registers
  These are specialized registers used for managing memory access based on the region required by the program.
  They are (CS, DS, ES, SS, FS, GS)
  Each segments register is 16 bits wide.
More on general purpose registers: https://en.wikipedia.org/wiki/Processor_register#GPR

## Slide 14
General Purpose Registers
The General purpose registers are as follows:
EAX – Accumulator (used in mathematical calculations, and for the return value of a function returns) ([EAX 32 bits] – [AX 16 bits] – [AH and AL each 8 bits])
EDX – Used alongside EAX during addition or multiplication. As well used in division calculation to hold remainder.
EBX – Extra register. Pointer to data in DS segment
ECX – Used as a counter for string and loop operations
EBP – Frame register, used to demark the end of a functions stack region. (BP – Base Pointer).
ESP – The stack pointer, stores the address of the top of the stack frame. It decrements each time new values get placed on the stack. (SP – Stack Pointer)
EDI – Used in array operation and holds the address of the Destination array. (DI - Destination Index).
ESI – Used in array operation and holds the address of the Source array. (SI - Source Index).

## Slide 15
General Purpose Registers – x64
The x64 architecture keeps the same General purpose registers but add an R-prefix (for "register") as follows:
  RAX RCX RDX RBX RSP RBP RSI RDI
    They are encoded as R0-R7 in the order shown above.
    This order is harder to remember so stick to the historical names.
  And a few extra were added: R8-R15
    No special purpose
In addition, an addressing mode was added to allow memory references relative to RIP (the Instruction Pointer) to ease the implementation of Position-independent code (PIC) used in shared libraries in some operating systems.

## Slide 16
Instruction Register vs Pointer
In the x86/x86_64 architecture the instruction register (IR) holds the current instruction to be executed or decoded. It is not the Instruction Pointer (IP).
The IP holds the address of the next instruction to be executed. If an exploit is able to redirect the Instruction Pointer to an address where an exploit is currently residing the CPU will oblige and happily execute the instructions at that location.
How can the IR or IP be manipulated in the x86 architecture?
What methods can be used to protect these registers?

## Slide 17
Segment Register1
A segment refers to a region of memory. The segments that normally get generated are code, data (read-only, import, export etc), stack. There can be others but at a minimum these will be present. The segment registers is used to access these segments of the running process in virtual memory (RAM).
CS – Refers to the code segment. Code or instructions are what the CPU executes
DS – Refers to the data segment. Data can be read only, or read and write, and is what the instructions will operate on.
SS – Refers to the stack segment. Data that is used within a function.
ES, FS, GS – Extra segments that do not have any specific purpose in the IA-32. In x64 FS and GS have some special purpose; related to the OS data structures.

## Slide 18
Segment Registers - Segmentation
Segmentation is a memory management approach used to allocate the physical memory of the computer. System memory is abstracted and is presented, to a process, as a collection of separate address spaces called segments.
Using the segment registers and an offset, a program can access any byte within a segment (CS:[AX] generates a 20 bit address).
What is the highest address that can be accessed by a 20 bits address?
Segmentation comes in a few flavor (Real mode, Protected are the most often discussed in x32). For x64, segmentation is available but is replaced with Paging.

## Slide 19
Segment register
In real mode there is no protection and it is possible that one process could encroach on another process' segment.
In protected mode, the mechanism available through the Global and Local Descriptor Table makes this more difficult for processes to encroach. If this happens there will be a Fault causing the CPU to be interrupted.
Are the segment registers vulnerable?
With newer Memory management techniques (paging) the segment registers don't perform the roles as they did with segmented memory. There are still a few Segment registers (FS and GS) that have special meaning in the PEB. These can be used to perform some exploits.
Can they be used in an inappropriate way?

## Slide 20
EFLAGS – RFLAGS (x64)
The EFLAGS register is a special purpose register. It consists of a set of flags read or set by the processor. If set, they dictate the approach in which the CPU completes a job. If read, the flag could be used by the programmer to determine the logic of the code to perform.
The EFlags register contains a group of status, control and system flags.
  Status Flags
    These are set by arithmetic or logic instructions
  Control
    Eg. Direction flags, used to determine if a string function should increment or decrement the offset of the variable.
  System
    Used by the Operating System and should not be modified by user application.
For more detail: see Intel manual Vol1, pg 3 -16 - Figure 3-8 EFLAGS Register

## Slide 21
EFLAGS – RFLAGS (add, sub, mul, div)
A few commons flags to be on the lookout for as the course progresses:
CF – Carry Flag: set if the arithmetic operation generates a carry or borrow from the MSB (unsigned)
ZF – Zero Flag: set if the arithmetic operation resulted in zero.
OF – Overflow Flag: Set if the resulting number is too large a positive or too small a negative number to be stored in the resulting memory. (signed)
DF – Direction Flag: Used to manipulate string instructions
SF – Sign Flag: Did the operation generate a negative number.
The System group of Flags are rarely accessed directly but possess a wealth of information especially for debugging and privilege level of running application.
See pages 80-82

## Slide 22
EFLAGS - RFLAGS

## Slide 23
64 bit Mode Execution Environment

## Slide 24
Instructions are represented symbolically via assembly language with the following format:
label: mnemonic argument1, argument2, argument3
label is an identifier which is followed by a colon.
mnemonic is a reserved name for a class of instruction opcodes which have the same function.
The operands argument1, argument2, and argument3 are optional. There may be from zero to three operands, depending on the opcode.
When two operands are present in an arithmetic or logical instruction, the right operand is the source and the left operand is the destination.
e.g
mov rax, 0x1
add rax, 0x2
Instruction Operands

## Slide 25: Operand Size
In 64-bit mode, the default address size is 64 bits and the default operand size is 32 bits. Defaults can be overridden using prefixes.
Address-size and operand-size prefixes allow mixing of 32/64-bit data and 32/64-bit addresses on an instruction-by-instruction basis.

## Slide 26
Addressing Modes
What are addressing modes? (page 88, 527)
They represent the format of the instruction and assist in determining what should happen in calculating the offsets or addresses required when reading or writing data. Think in reference to the source operand!!!
The addressing mode to be investigated are as follows:
Immediate
Direct
Indirect (load instruction)
Register
Register Indirect
Register Indirect with Displacement

## Slide 27
Addressing Modes
Here is a visual aide to help in understanding the different addressing modes

## Slide 28
Addressing Modes
Here a few instructions with the addressing modes to demonstrate how they would be used:
mov EAX, 0x54 (values/data are a part of the instruction) - immediate
mov EAX, [0x11223344] (The offset value is a part of the instruction) - Direct
add EAX, EBX (The offset is stored in a register) - Register
sub EAX, [ECX] - Register indirect
mov EBX, 0x20[EAX] ; common form mov EBX, [EAX + 20] (The value returned at the address register+offset) – register indirect with displacement
Indirect does not appear to be an addressing mode of the 80x86 architecture.

## Slide 29: Immediate Operand
Some instructions use data encoded in the instruction itself as a source operand. These operands are called immediate
e.g the following ADD instruction adds immediate value of 20 to the contents of the RAX register:
ADD RAX, 20

## Slide 30: Operand Addressing
IA-32 machine-instructions act on zero or more operands. Some operands are specified explicitly and others are implicit. The data for a source operand can be located in:
  1. the instruction itself (an immediate operand)
  2. a register
  3. a memory location
  4. an I/O port
When an instruction returns data to a destination operand, it can be returned to:
1. a register
2. a memory location
3. an I/O port

## Slide 31
Direct Address Diagram

## Slide 32
Indirect Address Diagram

## Slide 33
Mov instruction transfer data referred by second operand (i.e. register’s content, memory content, or an immediate value) into the location referred to by its first operand (i.e. a register or memory).
register-to-register is possible
memory-to-memory moves are not possible. In cases where memory transfers are desired, the source memory contents must first be loaded into a register, then can be stored to the destination memory address.
MOV Instruction

## Slide 34
  Syntax
  MOV register, register
  MOV register, immediate
  MOV memory, immediate
  MOV register, memory
  MOV memory, register
Read Intel Data Transfer Instructions
Intel Manual Vol 1 Chapter 5 - 5.1.1
MOV Instruction Forms

## Slide 35
The Netwide Assembler (NASM) is an assembler and disassembler for the Intel x86 architecture. It can be used to write 16-bit, 32-bit and 64-bit programs. NASM is considered to be one of the most popular assemblers. It can be used in Linux and Windows assemblers and debuggers
AT&T –GNU Assembler part of gcc compiler often used by Linux developers. Default for most Linux distributions
AT&T vs NASM -Assembler

## Slide 36
Syntax differences:
NASM
<mnemonic> <destination> <source> ; <comment>
e.g
mov eax, 0x12 ; stores immediate value 0x12 into 32 bit register eax
push rax ; pushes the value of 64 bit register rax into the stack
AT&T
<mnemonic> <source> <destination> # <comment>
e.g
movl $7, %eax # copies immediate value 7 into 32 bit register eax
push %rax
% means indirect operand $ means immediate operand
AT&T vs NASM

## Slide 37
AT&T vs NASM

## Slide 38
CPUID instruction provides an interface for querying information about x86 CPU such as: processor type and whether advanced features such as MMX/SSE are implemented.
CPUID does no have operands but affects 4 registers EAX, EBX, ECX and EDX. It returns processor identification and feature information to the EAX, EBX, ECX, and EDX registers, as determined by input entered in EAX
CPUID implicitly uses the EAX register to determine the main category of information returned. In Intel this EAX value is called CPUID leaf
CPUID should be called with EAX=0 first
If EAX=0 will return Manufacture ID string. A twelve-character ASCII string stored in EBX, EDX, ECX (in that order)
CPUID Instruction

## Slide 39
Examples of known Manufacture ID (12 characters) are
"AuthenticAMD" – AMD
“GenuineIntel" – Intel
"GenuineTMx86" – Transmeta
For Virtual Machines
" KVMKVMKVM " – KVM
"TCGTCGTCGTCG" – QEMU
"Microsoft Hv" – Microsoft Hyper-V or Windows Virtual PC
"VMwareVMware" – VMware
How many 32-bit registers are needed to store these characters?
CPUID Instruction

## Slide 40
e.g. When EAX =0 , GenuineIntel processor values returned in:
EBX =0x756e6547, EDX=0x49656e69 and ECX =0x6c65746e.
G e n u i n e I n t e l
Dec 71 101 110 117 105 110 101 73 110 116 101 108
Hex 47 65 6e 75 69 6e 65 49 6e 74 65 6c
CPUID Instruction

## Slide 41
The lower 32 bits of the file positions is used as the incoming %eax register
On Intel 64 processors, CPUID clears the high 32 bits of the RAX/RBX/RCX/RDX registers in all modes.
CPUID should be called with the most significant bit of EAX set. To obtain extended function information.
If EAX=1 CPUID will returned what is called signature of the CPU:
  Stepping ID (Product revision number) Bits 0-3
  Processor model Bits 4-7
  Processor Family Bits 8-11
  Processor Type Bits 12-13
  Other bits 14—31 are reserved or use for Extended IDs (other info needed to calculate processor, model, family
  Feature flags will be returned in registers EDX and ECX, and additional feature info in register EBX
CPUID Instruction

## Slide 42
Now is your Job (Lab 2) to read Intel Manual Volume 2A chapter 3 “Instructions Set reference A-L” 3-198 and learn more about CPUID instruction and investigate what processor info will be provided when EAX =2, EAX=3 and so on,
CPUID Instruction

## Slide 43
A way to access CPUID information is using Inline Assembly.
What is Inline Assembly ?
Assembly Instructions within another high-level programming language such as C/C++.
The inline assembler allows to embed assembly-language instructions in C and C++ source programs without extra assembly and link steps.
The inline assembler is built into the compiler
Inline assembly code can use any C or C++ variable or function name that is in scope. Because the assembly code can be mixed with C and C++ statements, it can do tasks that are impossible in C or C++
The __asm keyword invokes the inline assembler and it must be followed by an assembly instruction, a group of instructions enclosed in braces, or, at the very least, an empty pair of braces.
Inline Assembly in C

## Slide 44
  asm [volatile] ( “Template” : Output : Input : Registers to use (called or memory clobbers )
  Template use as strings and interpreted by assembler
  Template can be: %0 or %1and so on or %[name]
  int var=0;
  asm ( “add $5, %0” : =r (var) : “0”(var) );
Inline Assembly in C –asm syntax
gcc -g addinline.c -o addinline This will be compiled as AT&T

## Slide 45
  Volatile disables compiler’s optimizations and does not allow the compiler to remove the assembly block.
  output or input is specified with single letters such as: r for register m for memory address or I for immediate. These are architecture specific.
  Output
  It starts with = represents an output (only write) or + (input and output read and write)
  Input
  Define input variables that goes into registers
  Clobbers A comma-separated list of registers or other values changed by the Assembler Template,
  Used registers
  Modify flags
  If memory was modified
Inline Assembly in C

## Slide 46
Inline Assembly in C
  int var=0;
  asm volatile(“add $5, %0”: “+r” (var)); // + reads input (var) from register which is represented by %0 (whatever register was selected by the compiler) and add 5 to that register and write the result back into destination register
gcc -g addinline2.c -o addinline2 This will be compiled as AT&T
./addinline2
gdb ./addinline2

## Slide 47
Inline Assembly in C
gcc -g inline.c -o inline This will be compiled as AT&T
./inline
gdb ./inline

## Slide 48
Inline Assembly in C

## Slide 49
  Operand masm=att masm=intel
  %0 %%eax eax
  %1 $2 2
  move %%eax, %%ebx for AT&T
  move ebx, eax for Intel
Inline Assembly in C

## Slide 50
Inline Assembly in C
gcc -g inlinersp.c -o rsp –masm=intel
This will be compiled as Intel
./rsp

## Slide 51
Cache
Cache is memory built into the CPU, its presence helps to decrease processing time, increasing processor performance. Placing it in the CPU reduces the dependence on RAM during data processing.
RAM speed today is comparable to the CPU core speed. As of Jan 12, 2020 the fastest DDR4 RAM found online is rated for 3.2 GHz. That is amazing, so why cache if the speed is not a factor?
There's still the issue of transferring the information along the bus to the CPU. The bus latency could be a hinderance, reducing overall performance. Think General Purpose computer and contending tasks using the bus.
In comes cache which is smaller than RAM but is built from much faster technology and sits directly on the CPU. This decreases the latency, in effect speeding up retrieval and overall processing.

## Slide 52
Cache - Levels
Modern CPUs come with multiple levels of Cache [L1-L3] maybe more.
L1 is closest to the core and hence the fastest access times. Each CPU core will have a dedicated L1 cache.
Some architectures will use a separate cache for instructions and data. Why do this?
The other levels are usually shared between other cores, but is based on the manufacturers choice. L1 and L2 may be tied to the core for example.
There's also The Look-Aside Buffer (TLB) a part of the Memory Management Unit of the CPU used for further optimization of data retrieval.
Cache Type | Cache sizes
L1 | 32KB or 64KB (Intel i7)
L2 | 256KB (Intel i7) or 512KB
L3 | 4MB (Intel i7), 8MB or 32MB
Read more here: https://en.wikipedia.org/wiki/Nehalem_(microarchitecture)

## Slide 53
  CPUID to get cache L1 size
Inline Assembly in C

## Slide 54
Memory Management Unit
The memory management unit (MMU) is hardware within the computer tasked with enhancing memory accessing for the CPU. By maintaining a table of information and using specialized logic the MMU drastically helps reduce latency and memory faults.
It sits between physical memory and the CPU and also provides the CPU access to the TLB cache.
See vol. 3A 2-3 p.2849
Also p 790 - 791, 808, 815, 818

## Slide 55
References
Clock speed https://www.intel.ca/content/www/ca/en/gaming/resources/cpu-clock-speed.html
Inline Assembly Microsoft
https://docs.microsoft.com/en-us/cpp/assembler/inline/inline-assembler-overview?view=msvc-160
GNU Inline Assembly
https://gcc.gnu.org/onlinedocs/gcc/Extended-Asm.html
[1] https://software.intel.com/sites/default/files/managed/39/c5/325462-sdm-vol-1-2abcd-3abcd.pdf- pg 3-12 Vol 1
[2] https://software.intel.com/sites/default/files/managed/39/c5/325462-sdm-vol-1-2abcd-3abcd.pdf-pg 2-13 Vol 3A