## Slide 1
ITSC 204:
Computer Architecture
Module 3 Addendum: Floating Point Numbers Taxonomy
Notes: 1

## Slide 2
Floating point numbers
All numbers have a binary representation within the computer systems. To this point we have only dealt with analyzing and directly manipulating whole number (short, char, long, int etc) types.
The binary representation of these numbers is straightforward once you have a grasp of the basic concept of how to convert any number into its binary format.
Before getting into the method required to perform floating point calculations let's review converting whole number decimals to binary.

## Slide 3
Binary Conversion
Converting whole numbers:
Method 1: (know the powers of 2)
By knowing the power of 2 you can quickly determine the binary value
For example if your number was 12:
  The largest power of 2 that can fit into 12 is 3, so you write a 1 in that column and subtract 8 from the original number: 4 remains
  2 to the power of 2 is 4; so simply write 1 in that column subtract again leaves a zero result.
  Finish off by placing 0's in all other columns
This method is fairly straightforward.
Powers of 2 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
Decimal value | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
Binary value | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0

## Slide 4
Binary Conversion
Method 2:
Divide the number by 2 until you are left with a remainder of 0 or 1
Lets take the number 13
  132 = 6 remainder 1
  62 = 3 remainder 0
  32 = 1 remainder 1
  12 = 0 remainder 1
Writing the number with the most significant bit first we get 1101 (starting at the bottom); Decimal 13
Powers of 2 | 27 | 26 | 25 | 24 | 23 | 22 | 21 | 20
Decimal value | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
Binary value | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1

## Slide 5
Binary Conversion-Fractions
Applying the same logic we did with whole numbers to fractions we can see that the following table makes sense:
2 -1 is the same as saying . Using the same logic then we can see that saying 2 -4 is the same as saying .
Using Method 1 as before could be quite tedious as you can quickly see.
Powers of 2 | 2-1 | 2-2 | 2-3 | 2-4 | 2-5 | 2-6 | 2-7 | 2-8
Decimal value | 0.5 | 0.25 | 0.125 | 0.0625 | 0.03125 | 0.015625 | 0.0078125 | 0.00390625
Binary value | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0

## Slide 6
Binary Conversion-Fractions
Applying the following shortcut dramatically speeds up that process:
Multiply the fraction by 2
Leave the whole number 0 or 1
Take the remaining fractional part and repeat the multiplication
Repeat the process until you get 0 or a repeating sequence, stop based on your precision: Double 52 bits, Single 23
    0.75 x 2 = 1.5 – Leave 1
    0.5 x 2 = 1.0 – Leave 1
    0
The final value in binary is 0.110000…. (starting at the top)
Powers of 2 | 2-1 | 2-2 | 2-3 | 2-4 | 2-5 | 2-6 | 2-7 | 2-8
Decimal value | 0.5 | 0.25 | 0.125 | 0.0625 | 0.03125 | 0.015625 | 0.0078125 | 0.00390625
Binary value | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 7
Binary Conversion-Fractions
Confirm the following numbers:
200.25 – Whole number is easy => 1100 1000
0.25 x 2 = 0.5 Leave 0
0.5 x 2 = 1. 0 Leave 1
0
    Answer is: 1100 1000.01
4.525 – Whole number is easy => 0000 0100
0.525 x 2 = 1.05 Leave 1
0.05 x 2 = 0.1 Leave 0
0.1 x 2 = 0.2 Leave 0
0.2 x 2 = 0.4 Leave 0
0.4 x 2 = 0.8 Leave 0
0.8 x 2 = 1.6 Leave 1
0.6 x 2 = 1.2 Leave 1
0.2 x 2 = 0.4 Leave 0
0.4 x 2 = 0.8 Leave 0
0.8 x 2 = 1.6 Leave 1 (at this point we can see a repeat pattern)
Answer is: 0000 0100.100001100110011….

## Slide 8
IEEE 754 Standard
To store a floating point number in binary, a systematic way was needed. The IEEE 754 provides this method.
There are 2 main precision levels that are considered:
Single precision
  32 bits are used to represent the number.
  1 sign bit
  8 exponent bits
  23 fractional bits
Double precision
  64 bits are used to represent the number
  1 sign bit
  11 exponent bits
  52 fractional bits

## Slide 9
Single Precision
After converting our number to binary as shown in the previous slides, we next need to convert it to the IEEE 754 format. See the table below:
Sign bit
  The sign bit is a single bit of the 32 bit number that represents if the number is negative or positive. Zero mean positive and one means negative
Exponent bits:
  After converting the number to its binary fraction, the number needs to be placed into a normalized format. The format has a single bit (1) before the decimal place followed by all the fraction.
  Example 200.25 is 1100 1000. 01 normalized is 1.100 1000 01 x 27. This was achieved by shifting the decimal to the left 7 times. Positive 7 because we shifted to the left.
  IEEE 754 stipulates that before storing the value the exponent should be biased. Therefore we add 127 (bias) to the unbias exponent to get 134
Sign | Exponent | Fraction
1 bit | 8 bits | 23 bits
0 or 1 | 1 to 254 | 000 0000 0000 0000 0000 0000

## Slide 10
Single Precision
Fraction
  After normalization the bit (1) is dropped and only the fraction remains
  Example 200.25 is 1100 1000. 01 normalized is 1.100 1000 01 x 27.
  The fraction is then 100 1000 01
  This is padded, if needed, with 0's to fill in the remaining bits
  The above number would be 100 1000 0100 0000 0000 0000
  The formula is often seen to explain the process
  (-1)S x (1).fraction x 2exp -127
  S represents the sign bit; 1 causes the number to be negative. exp is the biased exponent subtracted from 127 to return the unbias exponent. (1) is returned before the fraction and the process is completed.
The table below shows the number 200.25 as a binary number.
Sign | Exponent | Fraction
1 bit | 8 bits | 23 bits
0 | 1000 0110 | 100 1000 0100 0000 0000 0000

## Slide 11
Single Precision - Example
Convert the number -0.15625
  0.15625 x 2 = 0.3125 Leave 0
  0.3125 x 2 = 0.625 Leave 0
  0.625 x 2 = 1.25 Leave 1
  0.25 x 2 = 0.5 Leave 0
  0.5 x 2 = 1.0 Leave 1
  0
  -0.15625 converted to binary is 0.00101
  Normalized: -1.01 x 2-3 unbiases exponent of -3 (shifting to the right)
  Biased exponent = exp + 127 (the unbiased exponent = biased exp – 127 )
  Sign bit is 1 for negative
  Biased exponent is 124 because -3 + 127 = 124
  The fraction is simply 01
The table below shows the final answer. In hexadecimal: 0xBE20 0000
Sign | Exponent | Fraction
1 bit | 8 bits | 23 bits
1 | 0111 1100 | 010 0000 0000 0000 0000 0000

## Slide 12
Double Precision
Repeating the steps of slide 9 - 11
Sign bit
  The sign bit is a single bit of the 32 bit number that represents if the number is negative or positive. Zero mean positive and one means negative
Exponent bits:
  After converting the number to its binary fraction, the number needs to be placed into a normalized format. The format has a single bit (1) before the decimal place followed by all the fraction.
  Example 200.25 is 1100 1000. 01 normalized is 1.100 1000 01 x 27. This was achieved by shifting the decimal to the left 7 times. Positive 7 because we shifted to the left.
  IEEE 754 stipulates that before storing the value the exponent should be biased. Therefore we add 1023 (bias) to the unbias exponent to get 1030
Sign | Exponent | Fraction
1 bit | 11 bits | 52 bits
0 or 1 | 1 to 2046 | 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000

## Slide 13
Double Precision
Fraction
  After normalization the bit (1) is dropped and only the fraction remains
  Example 200.25 is 1100 1000. 01 normalized is 1.1001 0000 1000 x 27.
  The fraction is then 100 1000 01
  This is padded, if needed, with 0's to fill in the remaining bits
  The above number would be 1001 0000 1000 000 0000 0000 …
  The formula is often seen to explain the process
  (-1)S x (1).fraction x 2exp -1023
  S represents the sign bit; 1 causes the number to be negative. exp is the biased exponent subtracted from 127 to return the unbias exponent. (1) is returned before the fraction and the process is completed.
The table below shows the number 200.25 as a binary number with double precision.
Sign | Exponent | Fraction
1 bit | 11 bits | 52 bits
0 | 100 0000 0110 | 1001 0000 1000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000

## Slide 14
Double Precision - Example
Convert the number -0.15625
  0.15625 x 2 = 0.3125 Leave 0
  0.3125 x 2 = 0.625 Leave 0
  0.625 x 2 = 1.25 Leave 1
  0.25 x 2 = 0.5 Leave 0
  0.5 x 2 = 1.0 Leave 1
  0
  -0.15625 converted to binary is 0.00101
  Normalized: -1.01 x 2-3 unbiases exponent of -3 (shifting to the right)
  Biased exponent = exp + 1023 (the unbiased exponent = biased exp – 1023 )
  Sign bit is 1 for negative
  Biased exponent is 1020 because -3 + 1023 = 1020
  The fraction is simply 01
The table below shows the final answer. In hexadecimal: 0xBFC4 0000 0000 0000
Sign | Exponent | Fraction
1 bit | 11 bits | 52 bits
1 | 011 1111 1100 | 0100 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000 0000

## Slide 15
Floating Point numbers
Single Precision

## Slide 16
Floating Point numbers
Double Precision

## Slide 17
Try the following
Convert the following to single precision IEEE 754 binary format:
7.25
100.453125
-20.3125
Convert the following to double precision IEEE 754 binary format:
-1.8125
10.03125
-0.3125
Ref Intel Manual Vol 1 chapter 4 page 99-100