## Slide 1
ITSC 204:
Computer Architecture
ARM Processor and Instruction Set
Notes: 1

## Slide 2
ARM Processor (features)
ARM stands for Advanced RISC Machine and is the name associated with the leading developer of RISC based processors.
First design in 1975 was 6502
  4000 transistors
  2 Mhz, 8 bits bus
  Took 26 cycles to add two integers
  Implemented in the BBC computer
In 1985 ARM1
  25000 transistors,
  8 MHz, 32 bit bus
  2 cycles to add two integers
  Implemented on Acorn Risc Machine
Example code
  ldr r0,[addressA]
  ldr r1,[addressB]
  add r2,r0,r1
  str r2,[addressC]

## Slide 3
ARM Processor (features)
Load-Store architecture - The processor operates on data held in registers. Data held in the register bank can be used multiple times without needing multiple memory accesses
In 2003 Firepath
  6 million transistors
  330 Mhz, 64-bit operations.
  It can use many registers with one instruction SIMD. ADDW r0/r1,r2/r3, r4/r5
ARM cores are widely used in smartphones, tablets and in most of embedded and IoT devices https://www.businessinsider.com/internet-of-things-devices-examples.
The ARM processor has been specifically designed to be small to reduce power consumption. This low power consumption and low heat production made the ARM the best design for mobile devices, which is why Apple implemented it in iPod.
Notes: https://www.businessinsider.com/internet-of-things-devices-examples

## Slide 4
ARM Processor (features)
iPhones, and Android phones were all based 32-bit ARM processors but in 2013 Apple introduced 64-bit capable A7 chip
Each instruction in RISC processors is a fixed length to allow the pipeline to fetch future instructions before decoding the current instruction.
Modern processors have pipelines that can execute multiple instructions at once, and may do so out of order.

## Slide 5
ARM Family
https://en.wikipedia.org/wiki/List_of_ARM_microarchitectures

## Slide 6
ARM Instruction Set
Unlike Intel, ARM does not manufacture chips, it just licenses the designs for other to optimize and manufacture.
What does this mean for the Instruction Set, it means that, there will be a consistency across all manufacturers in the language used to program these devices. This is because the manufacturers don't have to compete with each other on the core processor features, but instead can focus on the features supporting it.

## Slide 7
ARM Processor - Registers
In this course the focus will be on the SBC (single board computer) called the Raspberry Pi 4 (RPi 4). SoC – System on a Chip Cortex A53 –ARMv8-A
As discussed previously the processor has high speed memory locations inside it called registers. These registers provide the CPU with a scratchpad (temporary memory space) for its operations.
Here's a list of those registers for 32-bit system:
General Purpose: R0, R1, R2, R3, R4, R5, R6, R7, R8, R9, R10, R11, R12
Special Purpose: R13 Stack Pointer ,
R14 Linker register stores return address
  R15 Program Counter – Contains the address of next instruction to be fetched by processor

## Slide 8
You can see that the processor has far more general purpose registers than Intel. This is because it primarily performs its calculations (operations) in registers. It is called the Load-Store architecture as opposed to Intel which is a Register-Memory architecture.
Load-Store: https://en.wikipedia.org/wiki/Load-store_architecture
ARM Processor - Registers

## Slide 9
Armv8-A supports A32,T32 and A64 (AArch64)
Most A64 instructions operate on registers. It is fixed-length 32-bit instruction set.
The architecture provides 31 general purpose registers. 64-bit X register (X0..X30), or 32-bit W register (W0..W30).
SP Stack pointer
X30 is the LR link register. Contains return address
PC Program counter. Memory address of currently execution instruction
32 registers for floating points.
E.g. 32-bit integer addition: ADD W0, W1, W2 in this case the top 32 bits of the 64-bit register are zeroed
E.g. 64-bit integer addition: ADD X0, X1, X2
https://developer.arm.com/documentation/den0024/a/ARMv8-Registers
Registers for AArch64

## Slide 10
The ARM processor also has a specialty register that controls the behavior and reports the status of the processor. The status register is called Current Program Status Register (CPSR) and is like the Eflags register for the Intel processor.
The cpsr is divided into four fields: flags, status, extension, and control. In current designs the extension and status fields are reserved for future use. The control field contains the processor mode, state, and interrupt mask bits. The flags field contains the condition flags.
An instruction with a condition code is only executed if the condition code flags in the CPSR meets the specified condition. The instructions with s at the end such as adds or subs will update condition flags of current program status register (cpsr)
https://developer.arm.com/documentation/dui0068/b/arm-instruction-reference/conditional-execution?lang=en
ARM Processor – Special Register

## Slide 11
CPSR has many flags, but we will focus on a few:
N – Negative is set if the Most Significant Bit (MSB) of a number is set. This is due to an operation causing sign bit to be set. For a 32 bit register that will be bit 31.
  Eg. 0x1 – 0x1F, will result in 0xFFFF FFE2 (using 2's complement)
Z – Zero is set of the resulting operation (logic/mathematical) results in a value of zero.
  Eg 0x1 – 0x1, will result in 0x0 or 0x0 & 0x1 will result in 0x0
C – Carry is set if there is a carry from the MSB bit 31. This occurs if the operation create a number that is too large for the operand to hold in an unsigned mathematical operation.
  Eg 0x20 + 0xFFFF FFFF = 0x1 0000 001F r2 = 0x1000 0000 r3 = FFFF FFFF
V – Overflow is set when the result of a signed mathematical operation results in a number too large or too small.
  Eg (8bits) 0x7F + 0x7F result 0xFE (-2) or 0xFE - 0x7F result 0x7F (127)
I and F – Interrupt used to enable or disable interrupts
T – Thumb is used to indicate if the processor is in the Thumb state (16 bit operating mode)
Current Program Status Register

## Slide 12
ARM Instructions
The ARM processor also comes with it own set of assembly instructions. Below is a list of a few of them that will be discussed throughout the rest of this module:
  mov – copies values from one operand to another
  add, adc, adds – adds operands
  sub, subs– subtracts operands
  and – performs bitwise AND of operands
  orr – performs bitwise OR of operands
  eor – performs bitwise XOR of operands
  bl – performs a branch and link
  bic – performs bitwise bit clearing of operands
  cmp, tst – compare operands and sets bits in
  b, bxx – conditional and unconditional loops
  push, pop
  ldr, str
https://developer.arm.com/documentation/dui0068/b/arm-instruction-reference

## Slide 13
MOV data between operands
As mentioned previously the mov instruction is used to transfer data between operands. In most cases ARM only allows operation within the registers, the exception is for load and store operations which can move immediate data and data from memory. "mov" can have immediate values as an operand.
The instructions format of most ARM instructions will follow the form:
opcode <dest>, <Opr1>, <Opr2>
opcode <Rd>, <Rn>, <Rm>
Common abbreviation of the instruction is as follows: mov Rd, Rn, Rm.
Rn can be any of the registers (R0-R15) and Rm(Op2) can be a register or an immediate value. The immediate value is within the range of 0-255 maximum. The second operand Rm can be shifted. The registers can hold 32 bit values.
Examples:
mov r0, r5 | mov r1, #37
mov r1, #0x55 | 

## Slide 14
Addition
As stated before the format of most ARM instructions will follow the form:
opcode dest, src1, src2
The add instruction is used to place the summation of the source operands into the destination operand.
The adc instruction is a variant of the add instruction and simply adds the carry flag value to the final value placed into the destination operand.
IMPORTANT: To update the CPSR register after an addition operation use ADDS
These instructions allow for the addition of an immediate value.
Common abbreviation of the instruction add is as follows: add Rd, Rn, Op2
Op2 can be a register or immediate value.
Examples: lsl – logical shift left and alternatively (Logical shift Right – lsr)
add r1, r1, r5 | add r2, r1, #37
add r1, r5 (same as above) | add r1, r2, #0x55
add r1, r1, r5, lsl #3 | add r1, r1, r5, lsl #2
adc r1, r2, r3 (r1 = r2 + r3 + carry) | adc r1, r2, #3 (r1 = r2 + 3 +carry)

## Slide 15
Subtraction
The sub instruction is used to place the subtraction of the source operands into the destination operand.
Common abbreviation of the instruction add is as follows: sub Rd, Rn, Op2
Op2 can be a register or immediate value.
IMPORTANT: To update the CPSR register after a SUB use SUBS
Examples:
sub r1, r1, r5 | sub r2, r1, #37
sub r1, r1, r5, lsl #2 | sub r1, r1, r5, lsl #0x2
sub r1, r5 (same as above) | sub r1, r2, #0x55

## Slide 16
AND
The and instruction is used to place the bitwise result of and'ing the source operands, into the destination operand.
These instruction allow for the addition of an immediate value.
Common abbreviation of the instruction add is as follows: sub Rd, Rn, Op2
Op2 can be a register or immediate value.
Examples:
  and – performs bitwise AND of operands
and r1, r1, r5 | and r2, r1, #37
and r1, r5 (same as above) | and r1, r2, #0x55

## Slide 17
ORR and EOR
The ORR and XOR instruction is used to place the bitwise result of the OR, XOR'ing the source operands, into the destination operand.
These instruction allow for the manipulation with an immediate value.
Common abbreviation of the instruction add is as follows: orr Rd, Rn, Op2
Op2 can be a register or immediate value.
Examples:
orr r1, r1, r5 | orr r2, r1, #37
eor r1, r5, r2 | eor r1, r2, #0x55

## Slide 18
Branch Instructions
The BL instruction represent the Branch and Link. It transfers execution to the code being referenced by the operand and saves the return address to the Link register. This is in contrast to the Intel processor which saves the return address to the stack.
This is an unconditional branch and will be immediately executed. It has a similar behavior to the CALL instruction in Intel. An odd feature of the ARM processor though is that the value stored in the Link Register is the address of the instruction after the return address. To perform a return operation the BX instruction is used which perform a Branch Exchange. This places the address in the LR into the PC register.
Example:
next: bl fun1
  adds r0, r0, r2
  cmp r0, #0x10
  bne next
fun1: bx lr

## Slide 19
Branch Instructions - Conditional
Like the Intel JCC instructions the conditional branch instructions are affected by the status register. In the ARM processor the CPSR holds the flags being used to decide whether a BRANCH will be taken.
The instructions have the form: BXX where XX represents the conditions. Some examples include BCS, BEQ, BNE, BLS and BHI
Example of usage:
next:
  adds r0, r0, r2
  cmp r0, #0x10
  bne next

## Slide 20
The BIC (Bit Clear) instruction used to clear, (make a bit zero), 1 or multiple bits.
  It does so by performing AND of operand 1 with the Negation of operand 2.
  For example: bic R0, R1, #0x3;
  If the value in R1 was 0xFF the result of the following operation would be stored in R0.
Compare and Test behave exactly like their intel twins.
  CMP takes the values of the operands, simulates a subtraction operation and updates the CPSR flags based on the result without modifying the registers involved.
  TST takes the values of the operands, simulates a bitwise AND operation and updates the CPSR flags based on the result without modifying the registers involved.
R1 | 0000 0000 1111 1111
0xFFFC | 1111 1111 1111 1100 - (this is the negated value of 0x3)
R0 | 0000 00001111 1100 (R0 would contain 0xFC)
Bit Clear and Testing Instructions

## Slide 21
Cross Compilation - Setup
Generally speaking the ARM platform you will be working is likely to be an embedded one. This means that memory is at a premium. This means ability to install all your tools to complete development and testing will be affected by the amount of storage available.
This doesn't take into consideration the amount of RAM or CPU speed.
On the other hand your laptop and desktop computers will have all of those resources in abundance. This creates a conundrum, how do you develop and test your code for your embedded system on a computer with a different architecture.
The solution cross compilation and the associated toolchain. We have seen so far that we can install the necessary development tools on Linux to compile our C code. These same open source tools are also available for ARM. There are many projects available to build your own toolchain, but to keep things simple, let's use the ones available in the Linux repository.
To install: sudo apt-update && sudo apt-get install gnu-arm-linux-gnueabihf

## Slide 22: ARM Processor
The future of Microprocessors by Sophie Wilson (ARM inventor)
  https://www.youtube.com/watch?v=_9mzmvhwMqw
Who invented ARM Processor?
  https://www.youtube.com/watch?v=nbNnNF9JHFQ

## Slide 23: Raspberry Pi OS
Raspberry Images – 32-bit
  https://www.raspberrypi.org/software/operating-systems/
64 bit OS for 64-bit Raspberry PI
  https://www.balena.io/os/#download