## Slide 1
ITSC 204:
Computer Architecture
ARM Software and Memory
Notes: 1

## Slide 2
Memory Mapped I/O
When the processor needs to access data it needs to consider where that data exists. Is it in the I/O space or is it in memory. The Intel processor makes that distinction clear; requesting data from either the available I/O ports using specialized instructions or Memory using mov instructions for example.
In the ARM processor there isn't a distinction between the two. Instead the system maps everything into memory. Memory mapped I/O is the term used to refer to I/O that is mapped into memory.
To access any of these regions requires that one read the Manual for that processor to determine where in memory a specific I/O device would be mapped. It means that it is also possible to copy data into a region to effect the change required, turning on a GPIO port etc.

## Slide 3
Memory Instructions
Instruction like mov, add and sub work on immediate and values in registers. The ARM processor allows for the direct access to memory through specialized instructions.
The Load and Store instructions provide this level of access.
To load values(data) from a memory location into a register: LDR R1, [R0]
The value located in memory address pointed in R0 will be loaded into the R1 register.
To store a value (data) contained in a register to memory: STR R1, [R0]
The content of R1 will be stored in memory at the address pointed by R0

## Slide 4: ARM LDR and STR instructions
ldr = Load Word
ldrh = Load unsigned Half Word
ldrsh = Load signed Half Word
ldrb = Load unsigned Byte
ldrsb = Load signed Bytes
str = Store Word
strh = Store unsigned Half Word
strsh = Store signed Half Word
strb = Store unsigned Byte
strsb = Store signed Byte

## Slide 5: ARM immediate value
ARM instructions are 32 bits long. The first 4 bits are for condition,
other bits are for operand, registers and other flags.
It remains a limited amount of bits for immediate values. Assembler
will try to find solution such as implementing ror instruction on the
value. If assembler cannot find solution it will generate an error
“invalid constant”
https://developer.arm.com/documentation/dui0040/d/Basic-Assembly-Language-Programming/Loading-constants-into-registers/Direct-loading-with-MOV-and-MVN

## Slide 6: ARM immediate value
It is not possible to load full 32 bit address at once.
e.g moving 511 mov r0,#511 will generate an error of “invalid constant”. To solve the problem we can use:
move r0,256 and add r0,255 or ldr r0,=511
For mov rd, #imm16 the value can be moved in groups by using lsl instruction
mov r0, #0x1234
mov r0, #0x5678 lsl, #16
mov r0, #0xabcd lsl, #32

## Slide 7
immediate as offset
  ldr r3,[r1,#4]
Register as offset
ldr r3, [r1,r2]
Scale Register as offset
  ldr r3, [r1,r2,lsl#2]
ARM Addressing Modes

## Slide 8
Preindex with writeback calculates an address from a base register plus address offset and then updates the address base register with the new address.
Preindex offset is the same as the preindex with writeback but does not update the address base register. The preindex mode is useful for accessing an element in a data structure
Postindex only updates the address base register after the address is used. The postindex and preindex with writeback modes are useful for traversing an array. Postindex useful to pop off the stack
ARM Memory Addressing Modes

## Slide 9
Preindex with writeback base address register is updated
ldr r0,[r1,#4]!
ldr r0,[r1,r2]!
ldr r0,[r1,r2,lsl#2]!
Preindex offset base address register is NOT updated
ldr r0,[r1,#4]
ldr r0,[r1,r2]
ldr r0,[r1,r2,lsl#2]
Postindex base address register is updated
ldr r0,[r1],#4
ldr r0,[r1]
ldr r0,[r1],r2,lsl#2
ARM Addressing Modes for ldr and str

## Slide 10
ARM Memory Addressing Modes

## Slide 11
PRE r0 = 0x00000000
r1 = 0x00090000
mem32[0x00009000] = 0x01010101
mem32[0x00009004] = 0x02020202
Preindexing with writeback: LDR r0, [r1, #4]!
POST(1) r0 = 0x02020202
r1 = 0x00009004
Preindexing: LDR r0, [r1, #4]
POST(2) r0 = 0x02020202
r1 = 0x00009000
LDR r0, [r1], #4
Postindexing: LDR r0, [r1], #4
POST(3) r0 = 0x01010101
r1 = 0x00009004
ARM Memory Addressing Modes

## Slide 12
When a function is called in ARM architecture, by convention, registers R0 to R3 are used to pass arguments to the function, and R0 is used to pass a result back to the callers. A function that needs more than 4 inputs uses the stack for the additional inputs.
bl label (call function) - Branch Instruction
bl instruction places the return address in the link register
bl set the PC register to the address of the function
After function code is executed bx lr to return to previous function
Procedure Call for ARM

## Slide 13
Stack Instructions
PUSH and POP are pseudo-instructions and are aliases for the following respectively:
STMDB R13!
LDMIA R13!
LDM is shorthand for Load Multiple Register, DB – Decrement before
STM is shorthand for Store Multiple Register, IA – Increment after
3. LDM and STM can update the base register. For the stack base register is usually
sp register .
4. The sp register can be used to push and pop many registers in one instruction
PUSH {R0-R2} – pushes the values in R0, R1 and R2 onto the stack
stmdb r13!, {r0-r2}
POP {R0-R2} – pops the values starting at the stack register into register RO,R1 and R2
ldmia r13!, {r0-r2}

## Slide 14
Stack Instructions
LDM and STM instructions can be used with the following address mode:
IA -Increment address After each transfer. This is the default, and can be omitted.
IB - Increment address Before each transfer (ARM only).
DA - Decrement address After each transfer (ARM only).
DB - Decrement address Before each transfer.
LDM r8,{r0,r2,r9} ; same as LDMIA
STMDB r1!,{r3-r6,r11,r12}

## Slide 15
Addressing Modes For Load-Store
mem32[0x80018] = 0x03
mem32[0x80014] = 0x02
mem32[0x80010] = 0x01
r0 = 0x00080010 r1 = 0x00000000 r2 = 0x00000000 r3 = 0x00000000
LDMIA r0!, {r1-r3}
r0 = 0x0008001c
r1 = 0x00000001 r2 = 0x00000002 r3 = 0x00000003

## Slide 16
Addressing Modes For Load-Store
LDMIB r0!, {r1-r3}
LDMIA r0!, {r1-r3}

## Slide 17
r0 = 0x00009000
r1 = 0x00000009 r2 = 0x00000008 r3 = 0x00000007
STMIB r0!, {r1-r3}
MOV r1, #1
MOV r2, #2
MOV r3, #3
r0 = 0x0000900c r1 = 0x00000001 r2 = 0x00000002 r3 = 0x00000003
LDMDA r0!, {r1-r3}
r0 = 0x00009000 r1 = 0x00000009 r2 = 0x00000008 r3 = 0x00000007
Addressing Modes For Load-Store

## Slide 18
The stack in ARM is implemented as:
Descending. The stack grows downwards
Ascending. The stack grows upwards.
Full stack. The sp register points to the last item in the stack
Empty stack. The sp register points to the next free space on the stack
Stack Implementation in ARM

## Slide 19
Stack Implementation in ARM
From: https://developer.arm.com/documentation/dui0473/c/writing-arm-assembly-language/stack-implementation-using-ldm-and-stm
STMFD sp!, {r0-r5} ; Push onto a Full Descending Stack
LDMFD sp!, {r0-r5} ; Pop from a Full Descending Stack

## Slide 20
0x80018 0x00000002
sp  0x80014 0x00000003
0x80010 empty
0x8000c empty
if r1=0x00000002 and r4=0x00000003
STMFD sp!,{r1,r4} same as STMDB sp!, {r1,r4}
0x80018 0x00000002
0x80014 0x00000003
0x80010 0x00000003
sp  0x8000c 0x00000002
Stack Implementation in ARM

## Slide 21
https://www.allaboutcircuits.com/uploads/articles/Introduction_to_ARM_Assembly3.png
ARM Instruction Set Format (ARM7TDMI)

## Slide 22
ARM Instruction Set Format (ARM7TDMI)

## Slide 23
ARM Opcode e.g. For ARMv7
ADD R0, R1, R2
Condition I Opcode S Rn Rd Op2
1110|00|0|0100|0|0001|0000|000000000010
ADDS R4, R6, #42
1110|00|1|0100|1|0110|0100|000000101010
I if set to 1 the second operand is an immediate value
S If set to 1 the conditions status can be updated
00 reserved bits