## Slide 1: ITSC 206: LAN Networking for Offensive and Defensive Environments
Lecture 2: Secure the Local Area Network. (LAN)

## Slide 2: Table of Contents
Review Lecture & Lab
MAC Address Spoofing
ARP Address Spoofing
VLAN Hopping
DHCP Starvation
DHCP Server Spoofing
IP Spoofing
STP Spoofing
Private VLan

## Slide 3: Review Lecture & Lab

## Slide 4: Review
Network Security
Threats
Defenses (Defense in Depth)
Wired vs Wireless Networks
Network Vulnerabilities
Security Toolbox
Lab: Architecture Review, Packet Investigation & Vulnerability Analysis

## Slide 5: Threats, Vulnerabilities, Safeguards & Assets
Assets
Data
Facilities
Hw/Sw
Safeguards
Safeguards
Vulnerability
Threat
Threat
Threat

## Slide 6: MAC Address Spoofing

## Slide 7: MAC Address Spoofing
Very simple network attack technique
Attacking device can spoof a MAC address, registering itself as a different network node on the switch
This network attack technique serves as the basis for many higher-level network attacks
  Including CAM overflow, ARP spoofing, DHCP starvation and DHCP server spoofing

## Slide 8: MAC Address Spoofing

## Slide 9: MAC Address Spoofing Prevention
To mitigate MAC address spoofing:
  Configure Port security on all access ports to limit the number of allowed MAC address registrations
  Configure the violation types and the aging timers
    Switch(config)# int range fa0/1-24
    Switch(config-if-range)# switchport mode access
    Switch(config-if-range)# switchport nonegotiate
    Switch# show interfaces truck
    Switch(config-if)# switchport port-security
    Switch(config-if)# switchport port-security maximum 3
    Switch(config-if)# switchport port-security mac-address sticky
    Switch(config-if)# switchport port-security mac-address 0016.cb96.9594
    Switch# switchport port-security violation {shutdown | restrict | protect}
    Switch(config)#vlan 666
    Switch(config)# int range fa0/2-24
    Switch(config-if-range)# switchport access vlan 666

## Slide 10
Discussion

## Slide 11: ARP Spoofing

## Slide 12: ARP Spoofing
Network attack designed to take over traffic for the targeted IP address (man-in-the-middle)
Relies on ARP protocol to associate the attacker’s MAC address to an IP address on the same LAN segment
Successful execution allows attacker to hijack network traffic for the targeted IP address
Particularly useful for spoofing a network gateway

## Slide 13: ARP Spoofing
ARP spoofing builds on MAC address spoofing
Can be achived by sending specially crafted G-ARP packets to announce the MAC address for the target IP address on a particular network port
By repeatedly sending G-ARP packets, the MAC address is repeatedly associated with the attacker’s network port in the CAM table
Also, other hosts on the network intercept and store the attacker’s MAC address for the target IP address

## Slide 14: ARP Spoofing

## Slide 15: ARP Spoofing Prevention
To mitigate ARP spoofing
  Similar to MAC Spoofing Mitigation; and
  Enable Dynamic ARP Inspection (DAI) on Switch
    Intercepts all ARP requests (DHCP snooping) and responses on untrusted ports prevents a class of man-in-the-middle attacks
    The switch drops ARP packet if the sender MAC address and sender IP address do not match an entry in the DHCP snooping bindings database
      ip arp inspection vlan
  Static ARP mappings.
    A static mapping associates an IP address to a MAC address on a VLAN.
    Useful when static IP addresses are used, DHCP snooping cannot be run, or other switches in the network do not run dynamic ARP inspection.

## Slide 16
Discussion

## Slide 17: VLAN Hopping

## Slide 18: VLAN Hopping
A layer 2 network attack that targets the switch to gain access to a VLAN that is not accessible.
2 Types of attacks:
  Posing as a switch connected with a VLAN trunk,
  Double-tagging a VLAN to “hop” to another VLAN.

## Slide 19: VLAN Hopping via Trunk Port
Posing as a switch, the attacking device can request the switch port to negotiate a trunk using Dynamic Trunking Protocol (DTP)
Once a trunk is established, the connected device can send and receive different VLAN traffic
Can access restricted VLANs (e.g., management VLAN)
This type of network attack is effective with physical access to the LAN environment

## Slide 20: VLAN Hopping via Trunk Port

## Slide 21: VLAN Hopping via Double Tagging
The double tagging attack is when connected to an interface in access mode with the same VLAN as the native untagged VLAN on the trunk.
The attacker sends a frame with two 802.1Q tags, the “inner” VLAN tag is the VLAN that we want to reach and the “outer” VLAN tag is the native VLAN.
When the switch receives the frame, it will remove the first (native VLAN) 802.1Q tag and forwards the frame with the second 802.1Q tag on its trunk interface(s).
The attacker has now “jumped” from the native VLAN to the victim’s VLAN. It’s a one way trip but it could be used perhaps for a DOS attack.

## Slide 22: VLAN Hopping via Double Tagging
Attack Device
Victim
Device
Switch 1
Switch 2
Tag
1, 20
IP
IP
Tag
20
IP
VLAN 20
VLAN 1

## Slide 23: VLAN Hopping Prevention
To mitigate VLAN hopping via trunk port:
  Similar to MAC Spoofing Mitigation; and
  Do not put any hosts on VLAN 1 (the default VLAN);
  Change the native VLAN on all trunk ports to an unused VLAN ID;
  Explicit tagging on the native VLAN on all trunk ports.

## Slide 24
Discussion

## Slide 25: DHCP Starvation

## Slide 26: DHCP Starvation
Network attack targeting the exhaustion of a DHCP client IP from an authorized DHCP server
Using MAC address spoofing, an attacking device sends large numbers of DHCP requests using different “fake” MAC addresses
Once exhausted, the network DHCP server no longer has an available DHCP client IP to offer
This causes a Denial of Service (DoS) on the target network
DHCP starvation also serves as the basis of DHCP server spoofing attacks

## Slide 27: DHCP Starvation

## Slide 28: DHCP Starvation Prevention
To mitigate a DHCP starvation attack
  Similar to MAC Spoofing Mitigation; and
  Enable DHCP snooping on switch to prevent an unauthorized DHCP server from responding to DHCP requests

## Slide 29
Discussion

## Slide 30: DHCP Server Spoofing

## Slide 31: DHCP Server Spoofing
Network attack a rogue DHCP server poses as a legitimate DHCP server for the network segment
Since the DHCP server provides network gateway, DNS information, WPAD configuration, etc.,
DHCP server spoofing is the basis for many other higher-level network attacks, such as gateway spoofing, DNS spoofing and proxy spoofing

## Slide 32: DHCP Server Spoofing
DHCP server spoofing relies on DHCP starvation attacks
If DHCP starvation attack is successful, the legitimate DHCP server no longer offers DHCP client IPs
The rogue DHCP server starts offering DHCP servers on the network from its own pool of IP addresses (typically from the exhausted pool of IPs obtained from the DHCP starvation attack)

## Slide 33: DHCP Server Spoofing

## Slide 34: DHCP Server Spoofing Prevention
To mitigate DHCP server spoofing
  Similar to MAC Spoofing Mitigation; and
  Enable Port security on switch, limits the number of MAC addresses connected to switch port
    The attack relies on DHCP starvation attacks, mitigating DHCP starvation attacks also mitigates DHCP server spoofing
  Enable DHCP snooping on switch to prevent an unauthorized DHCP server from responding to DHCP requests

## Slide 35
Discussion

## Slide 36: IP Spoofing

## Slide 37: IP Spoofing
Network attack to hijack another IP address
Can hijack traffic destined for the target host
Builds on ARP spoofing to be successful
Attacker can repeatedly send G-ARP for a target IP address and redirects IP traffic to the attacker’s port
In its simplest form, attacker can change the IP address of a host and cause an IP address conflict (and DoS) on the target IP

## Slide 38: IP Spoofing

## Slide 39: IP Spoofing
To mitigate an IP spoofing attack
  Similar to MAC Spoofing Mitigation; and
  Use IP Source Guard to further restrict IP spoofing

## Slide 40
Discussion

## Slide 41: Spanning Tree Protocol Spoofing

## Slide 42: Spanning Tree Protocol Spoofing
Network attack that changes the STP topologies to force network traffic to traverse a rogue network device
By controlling the rogue network device, attacker can sniff all passing network traffic and perform man-in-the-middle attacks

## Slide 43: Spanning Tree Protocol Spoofing
Uses a rogue network device to pose as the ROOT bridge in a STP network
By injecting BPDU frames with the lowest priority, the rogue network device can become the elected ROOT bridge and change the topology in a STP network
Network traffic begins flowing through the ROOT bridge, allowing sniffing and man-in-the-middle attacks

## Slide 44: STP Spoofing

## Slide 45: STP Spoofing Prevention
To mitigate STP spoofing
  Similar to MAC Spoofing Mitigation
  Configure network ports with BPDU guard and ROOT guard
  Configure non-trunk ports to switch access ports

## Slide 46
Discussion

## Slide 47: Private VLAN

## Slide 48: Private VLAN
A private VLAN is used to provide additional segregation between all network hosts within the same VLAN
Especially useful for sensitive data servers that require port isolation to established secure hosting
A private VLAN includes Primary VLAN, Secondary VLAN (isolated and community), Promiscuous port, Isolated port and Community port

## Slide 49: Private VLAN
 | Isolated Port | Promiscuous Port | Community Port
Isolated Port | Deny | Permit | Deny
Promiscuous Port | Permit | Permit | Permit
Community Port | Deny | Permit | Permit

## Slide 50
Discussion

## Slide 51
© 2017, Southern Alberta Institute of Technology. All rights reserved.
This publication and materials herein are protected by applicable intellectual property laws. Unauthorized reproduction and distribution of this publication in whole or part is prohibited.
For more information, contact:
Director, Centre for Instructional Technology and Development
Southern Alberta Institute of Technology
1301 16 Ave. N.W., Calgary, AB T2M 0L4