## Slide 1: ITSC 206: Advanced Networking for Offensive and Defensive Environments
Lecture 3: Advanced Routing Protocols

## Slide 2: Table of Contents
Review Lab 2
Routing Information Protocol (RIP)
RIP Attacks
RIP Attack Mitigation
Open Shortest Path First (OSPF)
OSPF Attacks
OSPF Attack Mitigation
Border Gateway Protocol (BGP)
BGP Attack
BGP Mitigation

## Slide 3: Review Lecture & Lab

## Slide 4: Review
MAC Address Spoofing
ARP Address Spoofing
VLAN Hopping
DHCP Starvation
DHCP Server Spoofing
IP Spoofing
STP Spoofing
Private VLan
Lab: Secure LAN

## Slide 5: Routing Information Protocol (RIP)

## Slide 6: RIP
Routing Information Protocol (RIP) is a distance-vector routing protocol
It uses hop count as a metric to measure distance
Maximum number of hops allowed: 15
  A hop count of 16 is considered infinite and unreachable
Routing update sent out every 30 seconds using
  broadcast in version 1
  multicast in version 2

## Slide 7: RIP
The frequency of routing updates tends to be relatively noisy on network
Because updates are sent every 30 seconds, there is a tendency for all RIP routers to send updates within seconds of each other, creating a storm of updates every 30 seconds, particularly in version 1
Version 1 does not support router authentication, making it prone to attacks

## Slide 8: RIP: Split Horizon
Split horizon rule is used in RIP to prevent routing loop
Consider router A, B and C:
When A receives a route to C from B, it does not advertise back to B
This ensures B does not get an advertisement from A claiming that A has a route to C (via B) and creating a routing loop
A
B
C
X
Route to C

## Slide 9: RIP: Route Poisoning
Used to prevent router from routing packets through an invalid network
RIP uses route poisoning to announce a route is no longer valid and should be removed from routing table
It does it by announcing a route with hop count 16, which marks it as unreachable, causing all RIP routers to remove the route from routing table
A
B
C
Route to Z – hop 16
Remove route to Z
Remove route to Z
Route to Z – hop 16
Remove route to Z
Z
Route to Z Up/Down

## Slide 10: RIP Route Poisoning
RIP version 1 does not require authentication for route update
This allows rogue device to inject an illegitimate route into the routing tables of all participating RIP routers
Using route injection, an attacking device can poison the route to a network, effectively causing a denial of service attack

## Slide 11: RIP: Hold-Down Timer
Used to prevent any subsequent route updates after a network is announced as unreachable
Used to prevent conflicting routing updates until the network converges after a change
Default hold-down timer is set to 180 seconds
A
B
C
Route to Z – hop 16
Remove route to Z
Remove route to Z
Route to Z – hop 16
Remove route to Z
Z
Route to Z Up/Down

## Slide 12: RIP Route Injection
RIP version 1 does not require authentication for route update
This allows a rogue device to inject an illegitimate route into the routing tables of all participating RIP routers
Using route injection, an attacking device can inject a route to redirect all traffic through itself, and hijack network sessions by performing a man-in-the-middle attack

## Slide 13: RIP Attack Mitigation
Do not use RIP version 1 (no authentication mechanism, it is susceptible to network attacks)
Choose a complex password for authentication in version 2 to prevent brute force attacks with password file
An inefficient routing protocol that is also unsafe if misconfigured
Implement ACL to prevent other than neighbor to send updates
Deprecated, do not use RIP if at all possible.

## Slide 14
Discussion

## Slide 15: Border Gateway Protocol (BGP)

## Slide 16: Protocol Terminology
Interior Gateway Protocol (IGP)– the protocol used to exchange routing information within an autonomous system.
Exterior Routing Protocol (ERP)– the protocol used to transfer exchange information between autonomous systems.
Autonomous System (AS) – a set of routers with common routing rules, managed by one technical administrator and working with an IGP protocol (for routing within an AS, several IGP protocols can also be used).

## Slide 17: Protocol Terminology (cont)
Transit autonomous system (transit AS) – autonomous system, through which traffic is sent to other autonomous systems.
Path – a sequence consisting of autonomous systems numbers through which must pass to reach the destination network.
Path attributes (PA) – path characteristics that help to choose the best path.
BGP speaker – a router that runs BGP protocol.

## Slide 18: Protocol Terminology (cont)
Neighbors, peers – any two routers between which a TCP connection for exchanging routing information is open.
Network layer information about network availability (Network Layer Reachability Information, NLRI) – IP prefix and prefix length.
Operational algorithm -

## Slide 19: BGP WAN
AS64001
AS65001
router bgp 64001
bgp log-neighbor-changes
bgp maxas-limit 50
aggregate-address 172.16.0.0 255.255.252.0 summary-only
redistribute connected
redistribute static
neighbor 10.200.200.1 remote-as 65001
neighbor 10.200.200.1 soft-reconfiguration inbound
router bgp 65001
bgp log-neighbor-changes
bgp maxas-limit 50
aggregate-address 172.16.3.0 255.255.252.0 summary-only
redistribute connected
redistribute static
neighbor 10.100.200.1 remote-as 64001
neighbor 10.100.200.1 soft-reconfiguration inbound

## Slide 20: Border Gateway Protocol (BGP)
Standardized protocol used to exchange routing information between AS (Autonomous System) on the Internet
Used mostly in edge routers
BGP peers are set up manually between edge routers to exchange routing information
As the AS learns of a new route, the routing information is propagated to all peers
All learned routes are then processed and stored in RIB (Routing Information Base)

## Slide 21: BGP – Best Path Selection Order
Algorithm not standardized, Cisco IOS selection order is
  Don't consider routes if can't reach next-hop
  Weight (highest)
  Locally significant Cisco proprietary attribute
  Local Preference (highest)
  Locally originated routes
  AS-Path (shortest)
  Origin (lowest)
  MED (lowest)
  EBGP learned routes over iBGP learned routes
  Smallest IGP metric to next-hop value
Algorithm runs top down until a deciding match occurs
Other tie-breaking checks occur if no bestpath
  Oldest route, lowest Router-ID, lowest interface IP address, etc.

## Slide 22: BGP
Limited built-in mechanism to protect against attack or error from peers
No mechanism to protect against modification, deletion, forging or replaying of data
  Can be used as an attacking vector to destabilize a network
Advertises routes with any AS number
Can advertise an unassigned address prefix to perform prefix hijacking
Does not provide a global view of correct routing information to allow detection of invalid routes
Highly susceptible to false advertisement

## Slide 23: BGP Impactful Events
1997 AS 7007 – Leaked internal routing table, blackholed part of Internet
2005 Google – Misconfiguration or hacked
2008 Pakistan / Youtube blocking – Internal leaked to whole internet
2010 China – Internal leaked routes redirected a portion of Internet to China
2012 Australia – Filtering failure lead to 30 min outage

## Slide 24: BGP Hijacking (NLRI injection)
Since BGP is the standard protocol to exchange routing information on the Internet, hijacking BGP routes can have a great impact
If an edge router that exchanges routing information with an ISP using BGP is compromised, it is possible to broadcast external BGP announcement to perform BGP hijacking at the Internet
Previous BGP hijacking has been successful at rerouting traffic destined for a network to a controlled intermediate network device to perform man-in-the-middle attacks, or denial-of-service attacks

## Slide 25: BGP Attack Mitigation
Use peer authentication with MD5
Use a complex password
Use system monitoring to detect attacks
Route filtering on inbound announcement (on the ISP side)
See https://tools.ietf.org/html/draft-jdurand-bgp-security-00

## Slide 26: Discussion & Details
https://www.defcon.org/images/defcon-16/dc16-presentations/defcon-16-pilosov-kapela.pdf
https://bgpmon.net/how-the-internet-in-australia-went-down-under/

## Slide 27: Open Shortest Path First (OSPF)

## Slide 28: OSPF WAN
AS64001
AS65001
router ospf 10
router-id 172.16.3.1
auto-cost reference-bandwidth 10000
redistribute connected subnets
no passive-interface Fastethernet0
network 172.16.0.0 0.0.3.255 area 0
int Fa0
ip ospf network point-to-point
router ospf 10
router-id 172.16.7.1
auto-cost reference-bandwidth 10000
redistribute connected subnets
no passive-interface Fastethernet0
network 172.16.4.0 0.0.3.255 area 0
int Fa0
ip ospf network point-to-point

## Slide 29: OSPF
Open Shortest Path First (OSPF) is an algorithm to determine the best route to a particular network based on link state
Uses MD5 for authentication
Link State Advertisement is used to communicate routing topology to other OSPF routers in the area
Maximum age of LSA is one hour
LSA uses sequence number to track updates. Larger sequence numbers indicate a fresher route

## Slide 30: OSPF Route Injection
OSPF network without authentication can become a vector of attack
Route injection can be performed to force traffic through a compromised router and perform man-in-the-middle attacks
Route injection can also be used to blackhole access to networks, causing a denial-of-service attack
Other attacks include max age, sequence, max sequence

## Slide 31: OSPF Max Age Attack (DOS)
Maximum age of an LSA is 3,600 seconds
Attacker can clone a fake LSA packet pretending to be from router A with the different max-age set
Router A contests the change in age by sending a new message called “fight-back”
Attacker can continuously send false LSA packets to cause network confusion and subsequently put the network into a denial-of-service attack

## Slide 32: OSPF Sequence Attack (DOS)
Attacker can continuously send an LSA packet with a sequence number larger than the one from router A, which indicates a newer route is available
Router A will “fight back” with a newer sequence number LSA
Causes network to become unstable and subsequently put the network into a denial-of-service attack

## Slide 33: OSPF Authentication Attack
OSPF uses MD5 key based authentication as part of the standard
Provides good protection on OSPF routers and LSA exchanges
However, it can be cracked using special tools and password files

## Slide 34: OSPF Attack Mitigation
Authentication is the first line of defense
  Always configure the OSPF network with authentication
  Use complex password for OSPF authentication
Configure a passive interface on network interfaces that you don’t receive routing information (e.g., interface connecting to client networks)
Use system monitoring to detect attacks

## Slide 35
Discussion

## Slide 36
© 2017, Southern Alberta Institute of Technology. All rights reserved.
This publication and materials herein are protected by applicable intellectual property laws. Unauthorized reproduction and distribution of this publication in whole or part is prohibited.
For more information, contact:
Director, Centre for Instructional Technology and Development
Southern Alberta Institute of Technology
1301 16 Ave. N.W., Calgary, AB T2M 0L4