## Slide 1: ITSC 206: Advanced Networking for Offensive and Defensive Environments
Lecture 5: Network Address Translation and Web Proxies

## Slide 2: Table of Contents
Module 4 Review
Network Address Translation (NAT)
NAT Types (One-To-One, One-To-Many, SNAT, DNAT, PAT)
NAT Scenarios
Web Proxies
Web Proxy Types
  Explicit, Transparent, WCCP Redirection, Cloud
Web Proxy Features
  Cache, Categorization, AV Scan, BW Control

## Slide 3: Module 4: Review

## Slide 4: Review
Mid Term
NAC
  What is, How does it work,
  Examples
  Enterprise Usage
  Components
  Architecture
  Architecture Flaws
  Extensible Authentication Protocol

## Slide 5: Network Address Translation

## Slide 6: What is NAT?
Network Address Translation
The process of mapping one IP address to another by changing the IP address field in the Internet Protocol header
Performed as the IP packet passes through the NAT device

## Slide 7: What is NAT?
NAT is typically used to map public (internet routable) IP addresses to mask private (non-internet routable) IP addresses.
Example: A host on the network with the IP address 192.168.1.9 is not routable on the Internet. To communicate with hosts on the Internet, a NAT must be performed to translate the private IP address to the public address for the network. Once the IP packet is NAT, return traffic can route back to the network properly.

## Slide 8: Network Address Translation
Internal hosts can be assigned various internal (non-routeable) addresses eg
Range 1: Class A - 10.0.0.0 through 10.255.255.255 /8
Range 2: Class B - 172.16.0.0 through 172.31.255.255 / 12
Range 3: Class C - 192.168.0.0 through 192.168.255.255 /16
see RFC 1631
Increased the life span of IP v4
can be used for load balancing
can be used for back up links (multihoned)

## Slide 9: Network Address Translation
10.1.1.2
10.1.2.2
12.16.23.24
10.1.3.2
10.1.4.2
10.1.4.1/192.168.123.4
10.1.3.1/192/168.123.3
10.1.2.1/192.168.123.2
10.1.1.1/192.168.123.1
Remote
Access
Internal Servers
Internet
192.168.123.0/24

## Slide 10: Types of NAT

## Slide 11: One-to-One NAT
Simplest NAT type is one-to-one NAT (RFC2663)
Translates IP addresses in a one-to-one relationship
Useful to connect networks that have incompatible (public vs private) or overlapping IP addresses

## Slide 12: NAT One-to-One
12.16.23.24/30
Internet
192.168.123.0/24
DMZ
External
Internal
192.168.123.2
192.168.123.3
192.168.123.4
192.168.123.5
12.16.23.24
12.16.23.25
12.16.23.26
12.16.23.27

## Slide 13: One-to-Many NAT
Used to map many hosts on the private IP to the public Internet
Translates private IP addresses to a single IP address (usually a public address on the firewall’s external interface)
This is useful to connect private IP networks to the public Internet

## Slide 14: NAT One-to-Many
12.16.23.24/30
Internet
192.168.123.0/24
DMZ
External
Internal
192.168.123.2
12.16.23.24
12.16.23.25
12.16.23.26
12.16.23.27

## Slide 15: SNAT
Source NAT (SNAT) is the address translation done on the packet’s source IP address
Useful to perform source NAT to hide the source IP address from the destination host or network because of routing issues (private IP RFC1918) or overlapping issues

## Slide 16: DNAT
Destination NAT (DNAT) is the address translation done on the destination IP address of the packet
It is useful to perform destination NAT to translate allow access to the destination host or network that is non routable (Private IP RFC1918) or overlapping IP address

## Slide 17: Port Address Translation (PAT)
Since one-to-many NAT uses one IP address for many IPs, it is also necessary to translate the port number (TCP or UDP) to create a distinct combination of IP address and port information on the return packet so that it can be mapped back to the corresponding originating source
Example: Outbound connection to the Internet
Host A IP: 192.168.123.98 src port 6845
Host B IP: 192.168.123.99 src port 6845

## Slide 18: NAT One-to-Many
12.16.23.24/32
Internet
192.168.123.0/24
DMZ
External
Internal
192.168.123.98 dst port 80
192.168.123.99 dst port 443
192.168.123.100 dst port 21
192.168.123.101 dst port 22
12.16.23.24
dst port 80
dst port 443
dst port 21
dst port 22

## Slide 19: NAT Scenarios

## Slide 20: Hiding Behind a Public IP Address Using SNAT
Example: Outbound connection to the Internet
Host A IP: 192.168.123.98
Internet web server IP: 208.227.205.38
Firewall external interface IP: 193.38.56.247
Original Packet: Host A 192.168.123.98 > Internet web server 208.227.205.38
208.227.205.38
Internet
192.168.123.98
193.38.56.247/32

## Slide 21
After firewall NAT: Host A 193.38.56.247 > Internet web server 208.227.205.38
This allows host A with private IP 192.168.123.98 to access the Internet web server 208.227.205.38 using the firewall external IP by SNAT
The reply from the Internet web server can route back to the firewall external interface, then NAT back to host A on 192.168.123.98
Hiding Behind a Public IP Address Using SNAT
208.227.205.38
Internet
193.38.56.247/32
192.168.123.98

## Slide 22: Static NAT: Inbound to Web Server Using DNAT
Example: Inbound connection to web server from Internet
Web server IP: 192.168.1.34
Internet host IP: 209.89.23.29
Firewall external interface IP: 193.38.56.247
Original packet: Internet host 209.89.23.29 > Web server 193.38.56.247
208.98.23.29
Internet
193.38.56.247
192.168.1.34

## Slide 23
After firewall NAT: Internet host 209.89.23.29 > Web server 192.168.1.34
This allows the Internet host 209.89.23.29 to access the web server via the firewall’s external interface IP 193.38.56.247
The firewall performs DNAT to translate the destination IP to 192.168.1.34 and forwards the packet to the web server
Static NAT: Inbound to Web Server Using DNAT
208.98.23.29
Internet
193.38.56.247
192.168.1.34

## Slide 24: Port Address Translation (PAT)
Example: Outbound connection to the Internet
Host A IP: 192.168.1.98 src port 6845
Host B IP: 192.168.1.99 src port 6845
Internet web server IP: 208.98.23.29 dst port 80
Firewall external interface IP: 193.38.56.247
Original Packet: Host A 192.168.1.98:6845 > Internet web server 208.227.205.38:80

## Slide 25: PAT
After firewall NAT: Host A 193.38.56.247:23456 > Internet web server 208.98.23.29 :80
Original Packet: Host B 192.168.1.99:6845 > Internet web server 208.98.23.29 :80
After firewall NAT: Host B 193.38.56.247:23457 > Internet web server 208.98.23.29:80

## Slide 26: PAT
Since both hosts use TCP source port 6845 to go to the same web server (208.227.205.38), and both hosts’ source IP addresses are NAT to the firewall external interface IP, the source port number must be translated to different ports to differentiate the five tuples, to distinguish between the two connections and allow the firewall to route the return packet to the correct host

## Slide 27: PAT
Host A connection five tuples after NAT: 193.38.56.247:23456 > 208.227.205.38:80 TCP
Host B connection five tuples after NAT: 193.38.56.247:23457 > 208.227.205.38:80 TCP
208.98.23.29 port 80
Internet
193.38.56.247:23456
192.168.1.98 port 6845
192.168.1.99 port 6845
193.38.56.247:23457

## Slide 28
Discussion

## Slide 29: Web Proxies

## Slide 30: What is a Web Proxy?
Proxy is a device that acts as an intermediate to perform requests on behalf of the original requestor
As the name proxy implies, it represents the requestor and performs a request to a destination, and then relays the results back to the requestor
This is often seen as the “man-in-the-middle” method of accessing the web

## Slide 31: What is a Web Proxy?
A Web proxy is one that specifically proxies web (HTTP or HTTPS) requests
However, most web proxies today can also proxy other protocols, such as FTP, CIFS and streaming media
User
Proxy
Google
http://www.google.ca
http://www.google.ca
Google HTML page
Google HTML page
© 2017, Southern Alberta Institute of Technology

## Slide 32: Why Use a Web Proxy?
Protected hosts do not require a direct network connection to external Internet resources
With all outgoing web request proxied, firewall only needs to open Internet access for the proxy device, not the protected hosts; thus increasing security
All contents from web requests can be cached for performance enhancement

## Slide 33: Why Use a Web Proxy?
All contents from web requests can be scanned at the network level by antivirus software to provide an extra layer of defense.
Web requests can be filtered based on the categories assigned to the website. This is useful to control users’ Internet behavior (e.g., deny pornography browsing).

## Slide 34: HTTP Proxies
An HTTP proxy is the fundamental protocol for a web proxy
Detects and intercepts HTTP traffic by reading into the application header (layer 7), and proxies the connection at the application layer
An HTTP proxy presents itself as the destination web server to the connecting client computer and terminates the HTTP connection. Then, posing as a client computer, it re-establishes a new session to the real web server on the Internet

## Slide 35: HTTP Proxies
For every web request, there are actually two sessions established: one from client computer to the proxy and one from the proxy to web server
The web proxy, in turn, can see everything in the HTTP request, including the text, the images and the passwords!
Since an HTTP proxy has the ability to see all passing web traffic, you must consider the legal implications when using one

## Slide 36: HTTPS Proxies: SSL Interception
An HTTPS proxy is built on the HTTP proxy in a web proxy
It adds the SSL/TLS capability to the proxy engine
It performs HTTPS proxy service by detecting and intercepting HTTPS traffic, and performs the man-in-the-middle function to proxy the connection
Since SSL/TLS requires the careful handling of certificates, the HTTPS proxy is more complicated to set up:

## Slide 37: HTTPS Proxies: SSL Interception
  User accesses a web page using HTTPS protocol via web proxy.
  Web proxy receives and intercepts the HTTPS request.
  Web proxy creates a new session to the web page using HTTPS protocol.
  Web proxy receives the certificate from the web page.
  Web proxy rewrites the certificate for the web page with its own information.
  Web proxy presents the rewritten certificate to the user to establish a HTTPS session.

## Slide 38: HTTPS Proxies: SSL Interception
  User sends encrypted HTTPS request to web proxy, web proxy decrypts the HTTPS request and terminates the request.
  Web proxy re-encrypts the HTTPS request and sends it to the web page.
The reply from a web page uses the same decrypt-encrypt procedure in reverse
This setup requires the user computer to trust the certificate presented by the web proxy.
This can be achieved by pushing the proxy certificate to every client computer using Active Directory GPO.

## Slide 39
Discussion

## Slide 40: Types of Web Proxy

## Slide 41: Explicit Proxy
A proxy is usually installed offline, away from a network path to the Internet
Access to the web proxy is explicitly defined in client’s computers
Requires proxy configuration on every client computer that uses the proxy
The explicit proxy configuration can be deployed to domain computers via active directory GPO

## Slide 42: Explicit Proxy
Since the proxy setting is typically configured at the OS level, the OS can capture web traffic (HTTP and HTTPS) and redirect to web proxy regardless of the port number used by the web request (80, 443 or any other port numbers)
An offline proxy failure does not cause interruption to the Internet gateway

## Slide 43: Transparent Proxy
Usually installed as an inline appliance, directly in the network path to the Internet (e.g., inline with the Internet firewall)
Since a web request goes out through the firewall, it is intercepted and, in turn, served by the transparent proxy
Simplifies the deployment, since no extra configuration is required on client computers

## Slide 44: Transparent Proxy
The inline nature allows the transparent proxy to examine and capture all web requests regardless of the port numbers used (80, 443 or any other port numbers)
Inline nature also means a single point of failure to the Internet gateway
User
Proxy
Google
http://www.google.ca
http://www.google.ca
Google HTML page
Google HTML page

## Slide 45: Web Cache Communications Protocol (WCCP) Redirection
In WCCP redirection, the proxy is deployed offline
A WCCP-enabled router is configured to redirect web requests to the proxy device for service
Client computers do not require extra configuration to use WCCP redirection

## Slide 46: WCCP Redirection
Since the proxy is deployed offline, there is no interruption to Internet gateway in case of proxy failure
WCCP router must be configured to redirect web request based on specified port number (e.g., 80 and 443), therefore missing other web requests that use non-standard ports (e.g., 8080 or 8888)

## Slide 47: Cloud-Based Proxy
Cloud based solution is suitable for proxying web requests for remote users with Internet access
Provides the same level of proxy protection as one inside the corporate network
Client computer is explicitly configured to use the cloud-based proxy when possible, and to default to direct Internet access when proxy is unreachable

## Slide 48: Web Proxy Features

## Slide 49: Web Cache
One of the main benefits of using a web proxy is the ability to cache web content
Statistically speaking, a good percentage of web requests are duplicates
When web caching enabled, duplicate requests can be served from cache memory, not the Internet
Saves valuable bandwidth and speeds up content fetch time

## Slide 50: Web Categorization
Another benefit of web proxy is web categorization of content
Process of sorting every webpage available on the Internet into a collection of categories (typically from 80 to 100 categories)
Categories include gambling, nudity, financial services, malicious sources, scam/questionable and suspicious
Categorization is typically a paid subscription service, maintained by a reputable vendor

## Slide 51: Web Categorization
Vendor uses web crawlers and intelligent services to select categories for a webpage
Subscriber can also submit categorization through portal if there is a dispute
As of 2016, Google has indexed 30 trillion web pages.
  Due to number of new webpages created daily, often difficult to categorize the entire Internet
  Many lesser known webpages are “unknown” until the crawl engine sweeps them up
Web categorization is and remains the most powerful tool for security administrators to control users’ browsing behavior

## Slide 52: Blacklist and Whitelist
In addition to web categorization, web proxies typically support blacklists and whitelists
A blacklist is a list of webpages (URLs) that a security administrator wishes to block, regardless of the web category. Often used to block known malicious and off-limits pages.
A whitelist is a list of webpages (URLs) that an administrator wishes to allow, regardless of the category. Often used to allow connections to trusted partner sites and pages.

## Slide 53: Blacklist and Whitelist
Blacklists and whitelists can create their own issues.
  Since blacklists and whitelists are static, abuse can result in stale records in the list, often running into the thousands.
  Becomes difficult to manage in the long run.
  Careful use and periodic house-cleaning is required for these lists to remain effective

## Slide 54: Antivirus Scanning
The third benefit of a web proxy is the ability to perform antivirus/antimalware scanning on web content received from the Internet
Since a web proxy is the man-in-the-middle, it sees all web content received from the Internet, and can scan the content before passing it on to client computers
Using the ICAP protocol, web content is passed to a dedicated appliance for antivirus scanning and results are passed to the proxy to allow or deny the web content to client computers

## Slide 55: Bandwidth Control
Web proxies can also control bandwidth usage within an environment
Similar to QoS, bandwidth control is used to ensure sufficient bandwidth is available for all network hosts, especially when Internet gateway bandwidth is slow (in 10s of Mbit/sec)
Can restrict bandwidth usage to content such as YouTube videos, which may not be business related but which use large amounts of bandwidth, choking the Internet for business critical applications

## Slide 56
Discussion

## Slide 57
© 2017, Southern Alberta Institute of Technology. All rights reserved.
This publication and materials herein are protected by applicable intellectual property laws. Unauthorized reproduction and distribution of this publication in whole or part is prohibited.
For more information, contact:
Director, Centre for Instructional Technology and Development
Southern Alberta Institute of Technology
1301 16 Ave. N.W., Calgary, AB T2M 0L4