## Slide 1: ITSC 206: Advanced Networking for Offensive and Defensive Environments
Lecture 6: Firewalls

## Slide 2: Tables of Contents
Review Module 5
Firewall Basics & Types
Firewall Placement (Architecture)
Demilitarized Zone
UTM and Other Firewall Services
Defense in Depth
Firewall Maintenance

## Slide 3: Review Module 5: NAT & Proxy

## Slide 4: Review Module 5
Network Address Translation (NAT)
NAT Types (One-To-One, One-To-Many, SNAT, DNAT, PAT)
NAT Scenarios
Web Proxies
Web Proxy Types
  Explicit, Transparent, WCCP Redirection, Cloud
Web Proxy Features
  Cache, Categorization, AV Scan, BW Control

## Slide 5: Firewall Basics

## Slide 6: What is a Firewall?
A firewall is typically a layer 3 network device that filters traffic (layer 3 and above) in and out of a network
Generally used to prevent network attacks.
Computers inside a network usually do not have the necessary security protection from attacks and probes from outside networks.
A firewall is the first line of defence against these illegitimate attempts.

## Slide 7: Firewalls Are Policy
Active Policy Enforcement
Unenforceable Policy
Effects of Unenforceable Policy
Vectors for Unenforceable Policy

## Slide 8: Developing Policy
Identify Risks
Communicate Your Findings
Create or Update the Security Policy
Determine Policy Compliance
Sound Out Orgs Rules & Culture

## Slide 9: The Basic Five Tuples
All firewalls leverage the basic 5 tuples to perform filtering:
  Source IP address
  Destination IP address
  Source Port
  Destination Port
  Protocol Type (TCP, UDP, etc.)
The first 2 tuples define a layer 3 network connection between two network nodes that are communicating with each other

## Slide 10: The Basic Five Tuples cont
The next two tuples define a distinct layer 4 conversation between the two network nodes
The last tuple defines the protocol type of the conversation
  TCP (protocol number 6) is layer 4 connection-oriented
  UDP (protocol number 17) is layer 4 connectionless
  ICMP (protocol number 1) is layer 3 protocol that can be controlled by a firewall

## Slide 11: Network Traffic Filtering
A firewall is the necessary evil that guards the network like a gate. It stops most unwanted traffic from crossing the gate, allowing legitimate traffic through
A firewall rule defines a network connection based on the five tuples, along with an assigned action to be performed
  Actions can be Allow, Deny (Drop, Reset)

## Slide 12: Network Traffic Filtering
“Allow” passes inspected traffic through without any modification
“Deny” blocks traffic either by silently dropping the connection or by sending a reset to close the connection (TCP-RST)

## Slide 13: NAT and PAT
A firewall can also perform Network Address Translation (NAT) from a private IP address to a public IP address and vice versa in a one-to-one relationship
Port Address Translation (PAT) can be performed by a firewall to translate multiple IP addresses to a single IP address in a one-to-many relationship

## Slide 14: Network Address Translation
10.1.1.2
10.1.2.2
12.16.23.24
10.1.3.2
10.1.4.2
10.1.4.1/192.168.123.4
10.1.3.1/192.168.123.3
10.1.2.1/192.168.123.2
10.1.1.1/192.168.123.1
Remote
Access
Internal Servers
Internet
192.168.123.0/24

## Slide 15: Logging
A firewall has the capability to log all traffic (allow or deny) passing through it, for analysis purposes
Traffic logging allows security analysts to perform troubleshooting on the firewall rule set, as well as to post incident investigation

## Slide 16
Discussion

## Slide 17: Defense in Depth

## Slide 18: Defense in Depth
Defense in Depth is a concept borrowed from military
The idea is simple:
  Use multiple layers of defense to delay an incoming attack by yielding space to buy time
  Because attackers must work through different defense layers to access internal resources, the attack has higher chance of being detected, giving the organization time to respond
In network security, defense in depth includes multiple layers of firewalls, DMZ, IDS/IPS, antivirus, web filtering, etc.

## Slide 19
19
Defense In Depth (Remember)
Human
Defenses
Internal
Defenses
Perimeter
Defenses

## Slide 20
Discussion

## Slide 21: Firewall Defense

## Slide 22: Static Routes
In the internal network, it is standard practice to run routing protocols to maintain the network topology
However, it is a standard security practice to use static routes when routing traffic to any firewall
Static routes prevent the dynamics of routing protocols to route packets around firewalls in the event an alternative route is introduced (e.g., as a network attack)

## Slide 23: Firewall Management Access and Management Servers
Firewalls are essential tools for network security and should be hardened to protect them from unauthorized access
Individual firewalls should be configured to allow management access from dedicated jump servers or management servers
All other access to the firewall should be explicitly blocked and logged

## Slide 24: Antispoof
Antispoof is a mechanism used to detect unexpected traffic arriving at an interface, and then perform predefined actions
In a well-designed firewall deployment, each interface expects traffic from a well-defined collection of networks
Untrust interface expects traffic from the Internet (e.g., source IP = 0.0.0.0/0 minus the RFC1918 addresses)
DMZ interface expects traffic from the DMZ networks (e.g., source IP = 172.16.0.0/12)

## Slide 25: Antispoof
Trust interface expects traffic from the corporate networks (e.g., source IP = 10.0.0.0/8)
Example: Traffic with source IP 10.0.0.1 arriving at the Untrust interface triggers the antispoof
Ideally, drop all traffic triggering antispoof to prevent spoofing attacks

## Slide 26: Connection Table: Memory Issue
Every stateful firewall contains a connection table to track connections’ state
Established connections with continuous activity remain in the connection table until closed or dropped
Idle connections remain in the connection table until the timeout expires (default TCP timeout is 3,600 seconds)

## Slide 27: Connection table - memory issue
Connection table resides in the memory for fast process, thus every connection takes up available memory
Most firewalls have enough memory for million+ connections, but it is important to monitor the connection table to prevent memory exhaustion
When connection table is full, firewalls will continue to process existing connections but will not allow new connections to be established

## Slide 28: NAT Table, NAT Exhaustion
NAT (PAT) is used as a primary function in edge firewalls to allow communication to the Internet without assigning a public IP address to every network host
In small to medium enterprises, it is typical to configure firewall NAT with a single public IP address for outbound Internet access

## Slide 29: NAT Table, NAT Exhaustion
With a single public IP address, the available source port is 64 K
With a large number of active network connections, possible to exhaust all available source ports in the NAT table, causing the firewall to stop NAT for new connections
To prevent NAT exhaustion, use public IP pool instead of a single public IP address for NAT

## Slide 30: Throughput Considerations
Firewalls perform inspection at layer 4 and above
Because of the additional processing required for inspections, processing time is often penalized
Firewalls use CPU resources to process traffic. Too much throughput causes high CPU usage, resulting in dropped packets.
Typical firewall can inspect traffic in the range of 100 Mbps, while enterprise-class firewalls can inspect traffic in the range of 1 Gbps
Consider the throughput requirement when designing a firewall deployment

## Slide 31: Drop ANY ANY
Firewalls usually have an implicit DROP rule at the bottom of the rule set
Used to block all traffic passing through the firewall by default
However, it is useful to define an explicit DROP rule with manual logging for the purpose of troubleshooting

## Slide 32: The ANY ANY Rule
Often used in zone-based firewall, the ANY (source) ANY (destination) rule is handy to allow ANY traffic from one zone to another (e.g., Trust to Untrust)
In non-zone based firewalls, the ANY ANY rule is typically avoided, due to unexpected consequences in firewalls with multiple interfaces
For example, an ANY ANY rule can allow:
  Any host on the internal network to access the Internet (intended)
  Any host on the Internet to access the internal network (unintended)
It is a standard security practice not to use ANY in the five tuples. Always explicitly define them.

## Slide 33
Discussion

## Slide 34: Other Firewall Maintenance

## Slide 35: Other Firewall Maintenance
Back up and restore: An integral part of firewall management. Since firewalls are typically installed at the choke point within a network, it is crucial to have minimal downtime in the event of an incident.
Log management: Firewall logs can aid in troubleshooting connectivity issues, and serve as evidence in a security incident. Store all firewall logs in a secured repository and protect them from tampering (log manager, SIEM).
Ruleset version control: If firewall management supports version control, use it as a quick rollback mechanism in case of an issue with a change in firewall rules.

## Slide 36
Discussion

## Slide 37: Firewall Types

## Slide 38: Packet Filtering Firewall
The most basic type of firewall
Works at layer 3, similar to a router, with different networks on each interface
Filters traffic at layer 3 according to the five tuples in the rules
Does not maintain the state of the traffic. An administrator must create a rule for each traffic direction (initiate and return traffic)

## Slide 39: Packet Filtering Firewall
Example: To allow traffic from host A to web server B on TCP port 80 (HTTP) traffic, the administrator must create the following two rules:
  Host A on any port > Web Server B on port 80 on TCP protocol, allow (the “initiate” traffic)
  Web Server B on port 80 > Host A on any port on TCP protocol, allow (the “return” traffic)

## Slide 40
Network Filtering Layer 3/4

## Slide 41: Stateful Firewall
Has the intelligence to maintain the “state” of a network connection, and to account for the return traffic
Uses computing resources to examine a connection at the initiation phase, and tracks the connection in a connection table
When the return traffic arrives at the firewall, it performs a lookup at the connection table and automatically allows the return traffic through

## Slide 42: Stateful Firewalls
Example: To allow traffic from host A to web server B on TCP port 80 (HTTP) traffic, the administrator only needs to create one rule
  Host A on any port > Web Server B on port 80 on TCP protocol, allow (the “initiate” traffic)
Connection is maintained in the connection table and return traffic is automatically allowed through

## Slide 43
Stateful Filtering Still @ Layer 3/4

## Slide 44: Zone-Based Firewalls
Further development on firewalls allows the definition of network “zones” associated with individual interfaces
Trust zone: the network inside the firewall (the corporate network)
Untrust zone: the network outside the firewall (the Internet)
DMZ zone: the network dedicated between Trust zone and Untrust zone, mostly used for hosting web services

## Slide 45: Zone-Based Firewalls
Rules can be written specifically from one zone to another, simplifying rule set management
Example: To allow all outbound Internet traffic from a corporate network to the Internet:
  Trust zone to Untrust zone, allow ANY host to ANY destination on port 80 (HTTP)

## Slide 46: Transparent Firewall
Filters traffic based on firewall rules written with the five tuples, but examines and intercepts traffic at layer 2
Interfaces are grouped into bridges (layer 2), with the firewall inserted into the bridge transparently
Transparent firewalls do not require a layer 3 network for connectivity
  Useful for adding a firewall transparently inline into existing network without changing topology

## Slide 47
Transparent @ Layer 2

## Slide 48: Application Firewall (NextGen): L7
Application aware and understands application session information
Filters traffic based on layer 7 properties
Often user identity aware (AD integrated) to allow rule definition at user and group level
Example: Allow management group access to Facebook
  Allow AD_GRP_Management to www.facebook.com on port 80 and 443 (HTTP, HTTPS)

## Slide 49
Applicaton FW @ Layer 7

## Slide 50: UTM: Firewall and Other Services
Unified Threat Management is a traditional (stateful) firewall that can also perform other security functions, such as:
  Anti-Virus and/or Anti-Spam;
  Web Proxy;
  White/Black Listing
  Application Control / ID
  User Identity
  Intrusion Detection System and/or Intrusion Prevention System;
  Virtual Private Network and
  Web Filtering

## Slide 51: UTM: Firewall and Other Services cont
The “all-in-one” approach, functions enabled simply by purchasing a license
Ideal for small to medium enterprises due to reduced cost and reduced hardware footprint

## Slide 52
Discussion

## Slide 53: UTM and Other Firewall Services

## Slide 54: Web Proxies and Filtering
A web proxy is an intermediate device that “proxies” Internet web access to minimize corporate computers’ exposure to the Internet
Using a middleman approach, a web proxy can also cache the content of web pages for speed and bandwidth optimization, as well as perform web content filtering based on categorization (e.g., blocking pornography and malicious websites)

## Slide 55: Domain / IP Black Listing
Domain and/or IP black listing using threat intelligence to block external access
Vendor Threat Intel used

## Slide 56: Anti-Malware Tools
Since network traffic passes through the firewall, network based anti-malware tools can be applied to all network traffic, adding an extra layer of security against malware
Using both static (hash signature) and/or dynamic file analysis
Dynamic file analysis typically consists of file submission to service to perform various functionality up to and including file execution

## Slide 57: Anti-Spam Tools
Similar to anti-malware, network based anti-spam tools can be used on all email traffic passing through the firewall, adding an extra layer of security against spam and phishing attacks

## Slide 58: User Identity
Next Generation (NextGen) firewalls usually come with user identity awareness, to allow specific users or groups, instead of the traditional source IP address in the firewall rule
Typical integration includes Active Directory and/or LDAP
There are challenges with implementing this control effectively

## Slide 59: Application Control / ID
Use of firewall to identify the application transiting and confirm it behaves as expected (use of port / signaling / comms) and determine if operating within preset parameters
Limitations to depth of packet analysis by each technology vendor (Cisco FP vs Palo Alto vs Check Point)

## Slide 60: Intrusion Detection Prevention System
With visibility of all passing network traffic, network based IDS/IPS can also be deployed at the firewall
Typically signature based (Snort)

## Slide 61: VPN
Most firewalls include VPN termination as a standard feature
Basic implementation supports site-to-site VPN (e.g., IPSec) and remote access for users (e.g., SSLVPN)

## Slide 62: Web Filtering
Most UTM firewalls include Web filtering as a feature
Basic implementation supports site categorization and policy implementation

## Slide 63
Discussion

## Slide 64: Firewall Placement

## Slide 65: Edge Firewall
Installed at the edge of the corporate network, connecting to an external network (e.g., ISP or Partner network)

## Slide 66: Edge Firewall
10.1.1.2
10.1.2.2
12.16.23.24
10.1.3.2
10.1.4.2
10.1.4.1/192.168.123.4
10.1.3.1/192.168.123.3
10.1.2.1/192.168.123.2
10.1.1.1/192.168.123.1
Remote
Access
Internal Servers
Internet
192.168.123.0/24
ICS
Systems

## Slide 67: Internal Firewall
Installed inside the corporate network, to protect specific groups of networks (e.g., network access to data centre)

## Slide 68: Internal Firewall
10.1.1.2
10.1.2.2
12.16.23.24
10.1.3.2
10.1.4.2
10.1.4.1/192.168.123.4
10.1.3.1/192.168.123.3
10.1.2.1/192.168.123.2
10.1.1.1/192.168.123.1
Remote
Access
Internal Servers
Internet
192.168.123.0/24
ICS
Systems

## Slide 69: ICS Firewall
Internal firewall typically used to protect the ICS environment
A simpler way to access the ICS would be to allow direct access from a corporate network to an ICS network via the ICS firewall
However, this allows a compromised corporate asset to launch attacks on the ICS through the allowed communication channel on the ICS firewall
A more secure approach would be adding a DMZ between the corporate network and the ICS, using a security hardened jump server in the DMZ to access the ICS network

## Slide 70: ICS Firewall
10.1.1.2
10.1.2.2
12.16.23.24
10.1.3.2
10.1.4.2
10.1.4.1/192.168.123.4
10.1.3.1/192.168.123.3
10.1.2.1/192.168.123.2
10.1.1.1/192.168.123.1
Remote
Access
Internal Servers
Internet
192.168.123.0/24
ICS
Systems

## Slide 71: Host-Based Firewall
Installed on individual host (software) to protect traffic in and out of a host
It is effective at stopping attacks from within the network, where network-based security solutions do not have visibility
Windows firewall and Symantec Internet Security are examples of host-based firewalls

## Slide 72: Host Based Firewall
10.1.1.2
10.1.2.2
12.16.23.24
10.1.3.2
10.1.4.2
10.1.4.1/192.168.123.4
10.1.3.1/192.168.123.3
10.1.2.1/192.168.123.2
10.1.1.1/192.168.123.1
Remote
Access
Internal Servers
Internet
192.168.123.0/24
ICS
Systems

## Slide 73
Discussion

## Slide 74: Demilitarized Zone

## Slide 75: DMZ Firewall
10.1.1.2
10.1.2.2
12.16.23.24
10.1.3.2
10.1.4.2
10.1.4.1/192.168.123.4
10.1.3.1/192/168.123.3
10.1.2.1/192.168.123.2
10.1.1.1/192.168.123.1
Remote
Access
Internal Servers
Internet
192.168.123.0/24
ICS
Systems
172.16.0.0/24
External Facing Servers

## Slide 76: Demilitarized Zone
Also known as a perimeter network, is an isolated network that sits between the corporate trusted network and untrusted networks like the Internet or partner network
Useful buffer zone to allow an organization to install dedicated servers and services to gain access to resources in the other network, without exposing internal resources

## Slide 77: Demilitarized Zone
Example: Front-end email server in DMZ receives emails from the Internet, and then relays them to an internal email server through a secured channel.
  This allows an organization to receive emails from the Internet without directly exposing the internal email server to the Internet
Example: Web proxy in DMZ allows corporate computers to access the Internet as an intermediate device, without exposing the computers directly to the Internet

## Slide 78
Discussion

## Slide 79
© 2017, Southern Alberta Institute of Technology. All rights reserved.
This publication and materials herein are protected by applicable intellectual property laws. Unauthorized reproduction and distribution of this publication in whole or part is prohibited.
For more information, contact:
Director, Centre for Instructional Technology and Development
Southern Alberta Institute of Technology
1301 16 Ave. N.W., Calgary, AB T2M 0L4