## Slide 1
ITSC 203:
Offensive and Defensive Tool Construction
Module 6 Python Networking History and Taxonomy
Notes: 1

## Slide 2
Python Sockets
Regardless of the nature of the tools being built with python the analyst will find the need at some point the need to provide it network access.
To do this kind of work will require the use of the most widely used network module "socket".
Socket is the module in python that provides a sufficient number of classes and methods to complete many of the network facing challenges an analyst may have.
According to Justin Seitz, in Black Hat Python, there are times when you will be performing a Pentest and you will find that the only tool available is Python. This has the built-in module of socket ready for you to use. Allowing you to roll your own tool in the environment. This is the alternative to attempting to download a tool and risk being caught by an IPS/IDS.

## Slide 3
Sockets – software
A socket "is an internal endpoint for sending or receiving data"[1].
In essence a socket is the software representation of the RJ45 port or the wireless interface of the computer.
There are several types of sockets available to the developer to perform communication internally and over the internet. They are as follows:
  Datagram sockets (UDP) user datagram protocol:
  Stream sockets (TCP) Transport Control Protocol:
  Raw sockets
[1] https://en.Wikipedia.org/wiki/Network_socket

## Slide 4
Sockets Types
Datagram sockets:
  Connectionless communication meaning that the packets sent using this
  socket does not require confirmation of reception. There is no guarantee that it
  arrived. The ideal circumstance for this type of communication is for telephone
  conversations. If data was dropped or damaged in transmission, a request
  "please repeat that" would fix the problem. The alternative is the system would
  slow down trying to automate the retrieval of the information.
Stream sockets:
  connection oriented communication, meaning that the packets sent are
  confirmed for reception. They must be delivered and in a specific order.
  This is ideal in situations like browsing the web or file transfer
  applications.

## Slide 5
Sockets - Types
Raw Sockets:
"Allow direct sending and receiving of packets with any protocol specific
transport layer formatting" [1]. In the previously mentioned socket types the data
packets are encapsulated as described by the TCP/IP or OSI model. End to end
the applications take care of wrapping and unwrapping the headers associated.
The makes those headers invisible to the user.
In the case of the raw sockets, the user can manipulate the packets optionally adding the headers. This means end user has to know what to expect and
therefore parse the data to make it.
Security issues: Raw sockets get around Firewalls, because they don't flow through the normal layers of the TCP/IP model. From network to Application versus going through each layer.
[1] https://en.Wikipedia.org/wiki/Network_socket
[2] https://www.youtube.com/watch?v=BwfRsTK4PS0

## Slide 6
Sockets – First TCP Socket
  import socket
  host = input("Enter a host: ")
  port = int(input("Enter a port: "))
  client = socket.socket(socket.AF_INET, socket.SOCK_STREAM) # creates socket object
  client.connect((host, port)) # make a connection to the remote host
  client.send(f"GET / HTTP/1.1\r\nHost: {host}\r\n\r\n") # send HTTP request to remote host
  # The string being sent needs to be a bytes-like object not string
  # How can this be resolved? Convert the string to byte array!!!
  result = client.recv(4096) # Get result of the request, assuming the server has responded.
  # Retrieve up to 4kB of data from the input buffer
  print(result) # Confirm there was data received.
  Question: What happens if there is less than 4096 bytes of data in the buffer?
To test the above code works you will need a webserver. Luckily python comes with a built-in
simple Web Server for this situation. We will discuss how to create our own Server next.
Open a terminal and type:
student@ubuntu:~$ sudo python3 -m http.server --bind 127.0.0.1 8080

## Slide 7
TCP Server
from socket import *
from threading import *
import sys
def callback(client_sock):
request = client_sock.recv(1024)
print(f"[*] Received: {request}")
client_sock.send(b"ACK!")
client_sock.close()
host = ""
port = 0
if len(sys.argv) > 1:
host = sys.argv[1]
port = sys.argv[2]
else:
host = "localhost"
port = 20000
tcpsrv = socket(AF_INET, SOCK_STREAM)
# SOL_SOCKET level argument
# SO_REUSEADDR permits reuse - option to set
# 1 value of option to set
# see man setsockopt
tcpsrv.setsockopt(SOL_SOCKET, SO_REUSEADDR, 1) # https://www.gnu.org/software/libc/manual/html_node/Socket_002dLevel-Options.html#Socket_002dLevel-Options
tcpsrv.bind((host, port))
tcpsrv.listen(5) # backlog, the number of concurrent client before dropping request
print(f"[*] Listening on {host}:{port}")
while True:
client, address = tcpsrv.accept()
print(f"[*] Accepted connection from: {address[0]}:{address[1]}")
client_handler = Thread(target=callback, args=(client,))
client_handler.start()

## Slide 8
HTTP vs HTTPS
In the previous example the server that was accessed was using the HTTP protocol, which transfers in plain text. The example was kept simple to show the effect of a TCP packet. Keep in mind that this can't be use for secure communication as show in the output below. When the code was used to make an HTTPS request the following message was generated.
    HTTP/1.1 301 Moved permanently
    Location: https://www.sait.ca/
    Connection: close
    Cache-Control: no-cache
    Pragma: no-cache
The header is stating that the we were redirected to the secure website. Also, our client should not cache the response but to go and get a fresh copy from Location. Unfortunately, it is not possible to retrieve that site with the current configuration.
More socket information
  socket: https://docs.python.org/3.2/library/socket.html
  http: https://docs.python.org/3/library/http.client.html, https://docs.python.org/3/library/urllib.request.html#module-urllib.request
  https: https://docs.python.org/3/library/ssl.html

## Slide 9
UDP Server + Client
from socket import *
host = "localhost" #input("Enter host name: ")
port = 8000 # int(input("Enter port: "))
udpc = socket(AF_INET, SOCK_DGRAM)
udpc.sendto(b"gettime", (host, port))
msg, addr = udpc.recvfrom(1024)
print(msg, addr)
from socket import *
host = input("Enter host name: ")
port = int(input("Enter port: "))
udps = socket(AF_INET, SOCK_DGRAM)
udps.bind((' ',8000))
msg, addr = udps.recvfrom(1024)
print(msg)
udps.sendto(b"messages", addr)
The information presented above shows the client and server code for a UDP sockets. Notice the implementation is almost identical to the TCP socket. A few outstanding differences are clear.
  Notice the use of SOCK_DGRAM
  There are no connection statements

## Slide 10
Threads
As you begin to do more with your python tools you will at some point find situations in which the synchronous nature of the tool makes for a lengthy engagement. In situations like this you will need to run the tool multiple times providing each instance a different input or execute the tool with some asynchronous capability built in.
To operate asynchronously there are a few modules available the one that we will focus on is the threading module.
It is not a multiprocessing module, instead it allows one process container to manage multiple units of work (threads) to operate giving each thread a slice of the processor’s capability.

## Slide 11
Threads
IMPORTANT: Threading is not multiprocessing in the standard CPython implementation of Python which is installed by default on Linux.
Let’s take a look at a simple example of the threading module in operation.
import threading
def operations():
count = 0
while(count < 1000000):
if count % 45683 == 0:
print(f"{count}")
count += 1
thread1 = threading.Thread(target=operations )
thread2 = threading.Thread(target=operations )
Notes: Think CPU vs IO Bound.
CPU Bound - Heavy computation (3D graphics movement)
I/O Bound – Downloading or Uploading and copying

## Slide 12
Threads - Example
The problem with the previous example is that it doesn’t show us which thread is generating the output. We can make some assumptions based on output but the facility to get more details is available:
import threading
def operations():
count = 0
while(count < 1000000):
if count % 45683 == 0:
print(f"{count} {threading.currentThread().getName()}")
count += 1
thread1 = threading.Thread(target=operations, name="uniqueName" )
thread2 = threading.Thread(target=operations )
thread1.start()
thread2.start()
Notes: Think CPU vs IO Bound.
CPU Bound - Heavy computation (3D graphics movement)
I/O Bound – Downloading or Uploading and copying

## Slide 13
Threads - Example
Sometimes we need to pass some arguments the thread target during creation. This allows further manipulation of the thread behavior.
import threading
def operations(proto="udp", port=0):
count = 0
while(count < 1000000):
if count % 45683 == 0:
print(f"{count} {threading.currentThread().getName()}")
count += 1
print(f"Protocol: {proto} port: {port}")
thread1 = threading.Thread(target=operations, name="uniqueName")
thread2 = threading.Thread(target=operations, args=("tcp", 5544) )
thread1.start()
thread2.start()
Notes: Think CPU vs IO Bound.
CPU Bound - Heavy computation (3D graphics movement)
I/O Bound – Downloading or Uploading and copying

## Slide 14
References
https://docs.python.org/3/library/threading.html
https://stackoverflow.com/questions/46751725/input-and-print-thread-python
https://www.tutorialspoint.com/python/python_multithreading.htm